## Slide 1: Computer Abstractions and Technology

## Slide 2: Outline
Preliminary
Introduction
Eight Great Ideas in Computer Architecture
Below Your Program
Under the Covers
Technologies for Building Processors and Memory
Performance
The Power Wall
The Sea Change: The Switch from Uniprocessors to Multiprocessors
Real Stuff: Benchmarking the Intel Core i7
Fallacies and Pitfalls

## Slide 3: Preliminary
Computer architecture deals with the functional behavior of a computer systems viewed by a programmer
  The sizes of data types
  The types of operations that are supported
Computer organization deals with structural relationships that may not be visible to the programmer
  Interfaces to peripheral devices
  Clock frequency
  The technology used for the memory

## Slide 4: Introduction
Computer revolution makes novel applications feasible
  Computers in automobiles, cell phones, human genome project, World Wide Web (WWW), search engine
Classes of computing applications and their characteristics
  Personal computers (PCs)
    To emphasize delivery of good performance to single users at low cost
    Usually execute third-party software
  Servers
    Much larger computers usually are accessed only via a network
      To carry large workloads
        Single complex applications: usually a scientific or engineering application
        Many small jobs: a large web server
      Usually based on software from another source
        Database or simulation system
        Often modified or customized for a particular function

## Slide 5
Classes of computing applications and their characteristics (Cont.)
  Servers (Cont.)
    Much larger computers usually are accessed only via a network (Cont.)
      Built from the same basic technology as PCs
        To provide greater computing, storage, and I/O capacity
        To place a greater emphasis on dependability
    The widest range in cost and capability
      Low-end server
        Used for file storage, small business application, or simple web serving
      Supercomputers (the peak of computing capability)
        To consist of tens of thousands of processors and many terabytes of memory
        To cost tens to hundreds of millions of dollars
        Used for high-end scientific and engineering calculations
        A relatively small fraction of the servers and the overall computer market
Fig. 1.1 The 2X vs. 10Y bytes ambiguity was resolved by adding a binary notation for all the common size terms.

## Slide 6
Classes of computing applications and their characteristics (Cont.)
  Embedded computers
    The largest class of computers
    The widest range of application and performance
      Designed to run one application or one set of related applications
      Normally integrated with the hardware and delivered as a single system
    Embedded applications
      Often have unique application requirements that combine a minimum performance with stringent limitations on cost or power
      Often have lower tolerance for failure
      In consumer-oriented applications, dependability is achieved through simplicity
      Redundancy are often employed in large embedded systems
Welcome to the PostPC era
  PC  personal mobile device (PMD)
    A smart phone or a tablet computer
      Battery operated with wireless connectivity to the Internet
    Like PCs: users can download software (apps) to run on them
    Unlike PCs: keyboard and mouse  touch-sensitive screen or speech input

## Slide 7
Welcome to the PostPC era (Cont.)
  Server  cloud computing
    Warehouse scale computers (WSC)
      To rely upon giant datacenters
      Companies like Amazon and Google build these WSCs containing 100,000 servers and let companies rent portions of them
    Software as a Service (SaaS)
      To deliver software and data as a service over the Internet (cloud)
      Only a thin program such as a browser runs on local client devices
      Examples: web search, social networking
Fig. 1.2 The number manufactured per year of tablets and smart phones, which reflect the PostPC era, versus personal computers and traditional cell phones.

## Slide 8: Eight Great Ideas in Computer Architecture
Design for Moore’s law
  Moore’s law
    Integrated circuit resources double every 18~24 months
    Gordon Moore, 1965
  Designing for rapid change
    Computer architects must anticipate where the technology will be when the design finishes rather than design for where it starts
Use abstraction to simplify design
  Use abstractions to represent the design at different levels of representation
  Lower-level details are hidden to offer a simpler model at higher levels
Make the common case fast
  Making the common case fast will tend to enhance performance better than optimizing the rare case
  The common case is often simpler and easier to enhance than rare case

## Slide 9
Performance via parallelism
  To perform operations in parallel to get more performance
Performance via pipelining
  An implementation technique in which multiple instructions are overlapped in execution
Performance via prediction
  To guess and start working rather than wait until you know for sure
  Assumptions
    The recovery from a misprediction is not too expensive
    The prediction is relatively accurate
Hierarchy of memories
  Programmers want memory to be fast, large, and cheap
  Hierarchy of memories
    The fastest, smallest, and most expensive memory per bit at the top
    The slowest, largest, and cheapest per bit at the bottom
    Cache  main memory  disk

## Slide 10
Dependability via redundancy
  Computers need to be fast and dependable
  Since any physical device can fail, we make systems dependable by including redundant components
    To take over when a failure occurs
    To help detect failures

## Slide 11: Below Your Program
A simple view of hardware and software
  Application software
    To consists of millions of lines of code
    To rely on sophisticated software libraries that implement complex functions
  Systems software
    Operating system
      Handling basic input and output operations
      Allocating storage and memory
      Providing for protected sharing of the computer among multiple applications using it simultaneously
    Compiler
      To translate a program written in a high-level languages into instructions that the hardware can execute
  Hardware
    Can only execute extremely simple low-level instructions
Fig. 1.3 A simplified view of hardware and software as hierarchical layers, shown as concentric circles with hardware in the center and applications software outermost.

## Slide 12
From a high-level language to the language of hardware
  High-level programming language
    Composed of words and algebraic notation
    To provide for productivity and portability
    Can be translated by a compiler into assembly language
  Assembly language
    A symbolic representation of machine instructions
    Can be translated by an assembler into the binary version
  Machine language
    A binary representation of machine instruction
    Binary digit (bit)
Fig. 1.4 C program compiled into assembly language and then assembled into binary machine language.

## Slide 13: Under the Covers
Five classic components of a computer
  Input device, output device, memory, datapath, control
  Datapath and control are sometimes combined and called the processor
  This organization is independent of hardware technology
Fig. 1.5 The organization of a computer, showing the five classic components.

## Slide 14
Through the looking glass
  Liquid crystal displays (LCDs)
    A display technology using a thin layer of liquid ploymers that can be used to transmit or block light according to whether a charge is applied
  Active matrix display
    Using a transistor to control the transmission of light at each individual pixel
  Pixel
    The smallest individual picture element
    Can be represented as a matrix of bits (bit map)
      Depending on the size of the screen and the resolution
      To faithfully represent what is on the screen
      A color display might use 8 bits for each of he three colors (red, blue, and green)
    Raster refresh buffer (frame buffer): to store the bit map
Fig. 1.6 Each coordinate in the frame buffer on the left determines the shade of the corresponding coordinate for the raster scan CRT display on the right.

## Slide 15
Touchscreen
  Touch sensitive displays
  Capacitive sensing
    Can allow multiple touches simultaneously
Opening the box
  Integrated circuit (chip)
    A device combining dozens to millions of transistors
  Central processor unit (CPU): also called processor
    The active part of the computer which contains the datapath and control
    To add numbers, test numbers, signal I/O devices to active, and so on
  Dynamic random access memory (DRAM)
    Memory build as an integrated circuit
    To provide random access to any location
  Cache memory
    A small, fast memory that acts as a buffer for a slower, larger memory
  Static random access memory (SRAM)
    A faster and less dense memory than DRAM

## Slide 16
Opening the box (Cont.)
  Instruction set architecture (ISA): also called architecture
    An abstract interface between the hardware and the lowest-level software
    To encompass all the information necessary to write a machine language program that will run correctly
    Including instructions, registers, memory accesses, I/O, and so on
  Application binary interface (ABI)
    The user portion of the instruction set plus the operating system interfaces used by application programmers
    It define a standard for binary portability across computers
  Implementation
    Hardware that obeys the architecture abstraction
Fig. 1.8 The logic board of Apple iPad 2 in Fig. 1.7.
Fig. 1.7 Components of the Apple iPad 2 A1395.

## Slide 17
Fig. 1.9 The processor integrated circuit inside the A5 package.

## Slide 18
A safe place for data
  Volatile memory vs. nonvolatile memory
    Volatile memory
      To retain data only if it is receiving power
      Ex: SRAM, DRAM
    Nonvolatile memory
      To retain data even in the absence of a power source
      Ex: magnetic disk (hard disk), flash memory, DVD disk
  Primary memory vs. secondary memory
    Primary memory (main memory)
      Memory used to hold programs while they are running
      DRAMs have dominated main memory since 1975
      More expensive, smaller (size and capacity), more rugged, more power efficient
    Secondary memory
      Nonvolatile memory used to store programs and data between runs
      Magnetic disks dominated secondary memory before 1975
      Flash memory is the standard secondary memory for PMDs

## Slide 19
Communicating with other computers
  Networked computers have several advantages
    Communication, resource sharing, non-local access
  Local area network (LAN)
    Designed to carry data within a geographically confined area
    Typically within a single building
  Wide area network (WAN)
    A network extended over hundreds of kilometers that can span a continent
  Wireless network
    WiFi, Bluetooth…

## Slide 20: Technologies for Building Processors and Memory
The technologies that have been used over time
  Vacuum tube  transistor  integrated circuit (IC)  very large-scale integrated circuit (VLSI)  ultra large-scale integrated circuit (ULSI)
Fig. 1.10 Relative performance per unit cost of technologies used in computers over time.
Fig. 1.11 Growth of capacity per DRAM chip over time.

## Slide 21
The manufacture of a chip
  Terminologies
    Silicon
      A natural element that is a semiconductor
    Semiconductor
      A substance that does not conduct electricity well
    Silicon crystal ingot
      A rod composed of a silicon crystal
      8~12 inches in diameter, 12~24 inches long
    Wafer
      A slice from a silicon ingot no more than 0.1 inch thick
      Used to create chips
    Die (chip)
      The individual rectangular sections that are cut from a wafer
    Defect
      A microscopic flaw in a wafer or in patterning steps
      Can result in the failure of the die containing that defect
    Yield
      The percentage of good dies from the total number of dies on the wafer

## Slide 22
Fig. 1.12 The chip manufacturing process.
Fig. 1.13 A 12-inch (300 mm) wafer of Intel Core i7 (Courtesy Intel).

## Slide 23
The manufacture of a chip (Cont.)
  The cost of an integrated circuit
    Cost per die = Cost per wafer / (Dies per wafer  Yield)
    Dies per wafer  Wafer area / Die area

## Slide 24: Performance
Defining performance
  What is “one computer has better performance than another”?
  Example 1
    Highest cruising speed: BAC/Sud Concorde
    Longest cruising range: Douglas DC-8
    Largest capacity: Boeing 747
    To transport 450 passengers: Boeing 747, not BAC/Sud Concorde
  Example 2
    Running a program on two different computers
      The faster computer is the one that gets the job done first
    Running jobs on several servers submitted by many users
      The faster computer is the one that completes the most jobs

## Slide 25
Defining performance (Cont.)
  Response time vs. throughput
    Response time (execution time)
      The time between the start and completion of a task
      Including disk access, memory access, I/O activities, operating system overhead, CPU execution time, and so on
      An individual computer user is interested in reducing response time
    Throughput (bandwidth)
      The total amount of work done in a given time
      Datacenter managers are often interested in increasing throughput
  Example: throughput and response time
    Replacing the processor in a computer with a faster version
      Both response time and throughput are improved
    Adding additional processors to a system for parallel processing
      Throughput is increased
      If the demand for processing is almost as large as the throughput, the response time also can be improved

## Slide 26
Defining performance (Cont.)
  We are primarily concerned with response time
  To relate the performance of two different computers quantitatively
    X is n times faster than Y, X is n times as fast as Y
  Example: relative performance
    Problem
      Computer A runs a program in 10 sec, computer B runs the same program in 15 sec
      How much faster is A than B?
    Solution
      A is 1.5 times faster than B, or B is 1.5 times slower than A

## Slide 27
Defining performance (Cont.)
  Terminology
    Normally use the terminology faster than
    Improved performance  increased performance
    Improved execution time  decreased execution time
Measuring performance
  Time is the measure of computer performance
    Wall-clock time (response time, elapsed time)
      The total time to complete a task
      Including disk accesses, memory accesses, I/O activities, OS overhead…
    A processor may work on several programs simultaneously
      The system may try to optimize throughput rather than attempt to minimize the elapsed time for one program
    CPU execution time (CPU time)
      The time the CPU spends computing for a task
      Not include time spent waiting for I/O or running other programs
      User CPU time: the CPU time spent in a program itself
      System CPU time: the CPU time spent in the operating system performing tasks on behalf of the program

## Slide 28
Measuring performance (Cont.)
  Time is the measure of computer performance (Cont.)
    System performance: the elapsed time on an unloaded system
    CPU performance: user CPU time
  Other metrics
    Clock cycle (tick, clock tick, clock period, clock, cycle)
      The time for one clock period (ps)
    Clock rate
      The inverse of the clock period (Hz)
CPU performance and its factors
  To relate different performance metrics
    CPU execution time for a program equals to
      CPU clock cycles for a program  Clock cycle time
      CPU clock cycles for a program / Clock rate
    The hardware designer can improve performance by
      Reducing the length of the clock cycle
      Reducing the number of clock cycles required for a program
      Trade-off between above two factors

## Slide 29
CPU performance and its factors (Cont.)
  Example: improving performance
    Problem
      A program runs in 10 seconds on computer A, which has a 2 GHz clock
      We want to build a computer B that will run this program in 6 seconds
      To increase the clock rate is possible, but will require 1.2 times as many clock cycles as computer A
      What clock rate should computer B have?
    Solution
      CPU timeA = CPU clock cyclesA / Clock rateA
      10 = CPU clock cyclesA / 2  109  CPU clock cyclesA = 20  109 cycles
      CPU timeB = 1.2  CPU clock cyclesA / Clock rateB
      6 = 1.2  20  109 / Clock rateB  Clock rateB = 4 GHz
Instruction performance
  The execution time must depend on the number of instructions in a program
    CPU clock cycles required for a program
      Instructions for a program  Average clock cycles per instruction
    Clock cycles per instruction (CPI)
      The average number of clock cycles each instruction takes to execute
      One way to compare different implementations of the same ISA

## Slide 30
Instruction performance (Cont.)
  Example: using the performance equation
    Problem
      Computer A and B have the same ISA
      Computer A: clock cycle time 250 ps, CPI 2.0 for some program
      Computer B: clock cycle time 500 ps, CPI 1.2 for the same program
      Which computer is faster for this program and by how much?
    Solution
      Assume the program has I instruction
      CPU clock cyclesA = I  2.0 CPU clock cyclesB = I  1.2
      CPU timeA = I  2.0  250 = 500  I ps faster !
      CPU timeB = I  1.2  500 = 600  I ps
      Computer A is 1.2 times as fast as computer B for this program
The classic CPU performance equation
  Instruction count
    The number of instructions executed by the program
  CPU time
    Instruction count  CPI  Clock cycle time
    Instruction count  CPI / Clock rate

## Slide 31
The classic CPU performance equation (Cont.)
  Example: comparing code segments
    Problem
      Which code sequence executes the most instructions? Which will be faster? What is the CPI for each sequence?
    Solution
      The number of executed instructions
        Sequence 1: 2 + 1 + 2 = 5
        Sequence 2: 4 + 1 + 1 = 6 more !
      Execution time
        CPU clock cycles1 = (2  1) + (1  2) + (2  3) = 10 cycles
        CPU clock cycles2 = (4  1) + (1  2) + (1  3) = 9 cycles faster !
      CPI
        CPI1 = CPU clock cycles1 / Instruction count1 = 10/5 = 2
        CPI2 = CPU clock cycles2 / Instruction count2 = 9/6 = 1.5
 | CPI for each instruction class |  | 
 | A | B | C
CPI | 1 | 2 | 3
Code sequence | Instruction counts for each instruction class |  | 
 | A | B | C
1 | 2 | 1 | 2
2 | 4 | 1 | 1

## Slide 32
The classic CPU performance equation (Cont.)
  To combine all factors
    The only complete and reliable measure of performance is time
      Changing the instruction set to lower instruction count
       An organization with a slower clock cycle time or higher CPI
      CPI depends on type of instructions executed
       The fewest number of instructions may not be the fastest
Fig. 1.15 The basic components of performance and how each is measured.

## Slide 33
The classic CPU performance equation (Cont.)
  How to determine the value of factors
    CPU execution time
      Running the program
    Clock cycle time
      Usually be published for a computer
    Instruction count
      Depend on the architecture but not on the exact implementation
      Using software tools to profile the execution
      Simulator of the architecture
      Hardware counter
    CPI
      Depend on a wide variety of design details in the computer
      Detailed simulation of an implementation
      Hardware counter
      To look at the different types of instructions and using their individual clock cycle counts
  The danger of using only one factor to access performance
    All three components must be considered

## Slide 34
The classic CPU performance equation (Cont.)
  Major factors to affect CPI
    The performance of the pipeline
    The performance of the memory system

## Slide 35: The Power Wall
Clock rate vs. power
  Both increased rapidly for decades and then flattened off recently
  The reason they grew together
    Clock rate and power are correlated
  The reason for their recent slowing
    We have to run into the practical power limit for cooling commodity microprocessors
Fig. 1.16 Clock rate and power for Intel x86 microprocessors over eight generations and 25 years.

## Slide 36
The really critical resource is energy in the PostPC era
  Battery life can trump performance in the PMD
  Architects of WSCs try to reduce the costs of powering and cooling servers
  The energy metric joules is a better measure than a power rate like watts
In CMOS technology
  The primary source of energy consumption is dynamic energy, which is consumed when transistors switch states from 0 to 1 and vice versa
    Energy  Capacitive load  Voltage2
      The energy of a pulse during the logic transition of 0  1  0 or 1  0  1
    Energy  ½  Capacitive load  Voltage2
      The energy of a single transition
  The power required per transistor
    Energy  Capacitive load  Voltage2  Frequency switched
    Frequency switched is a function of the clock rate
    Capacitive load per transistor is a function of fanout and the technology
  Energy and thus power can be reduced by lowering the voltage
    The voltage was reduced about 15% per generation
    Voltages have gone from 5V to 1V in 20 years

## Slide 37
Example: relative power
  Problem
    A new processor with 85% capacitive load, voltage is reduced by 15%, and 15% shrink in frequency
    What is the impact on dynamic power?
  Solution
Problem today
  Further lower the voltage will make the transistors too leaky
    40% of the power consumption in server chips is due to leakage
    If transistors started leaking more, the whole process could become unwieldy
  Power reducing methods
    To attach large devices to increase cooling
      Too expensive for PCs and even servers, not to mention PMDs
    To turn off parts of the chip that are not used in a given clock cycle
  Computer designers slammed into a power wall
    A different path to design newer microprocessors

## Slide 38: The Sea Change: The Switch from Uniprocessors to Multiprocessors
Fig. 1.17 Growth in processor performance since the mid-1980s.

## Slide 39
Multicore microprocessor
  The improving rate in response time of programs has slowed down
    1.5  1.2 per year since 2002 for desktop microprocessor
  Since 2006, microprocessors  multiple processor per chip
    The benefit is often more on throughput than on response time
    Both desktop microprocessor and server
  For programmers to get significant improvement in response time
    In the past
      To rely on innovations in hardware, architecture, and compilers to double performance every 18 months
      Without having to change a line of code
    Today
      To rewrite programs to take advantage of multiple processors
      To continue to improve performance of their code as the number of cores increases
It is hard to write explicitly parallel programs
  Programming for performance
    The program need to be not only correct but also fast

## Slide 40
It is hard to write explicitly parallel programs (Cont.)
  Load balancing
    To divide an application so that each processor has roughly the same amount to do at the same time
    The overhead of scheduling and coordination
    Communication and synchronization overhead

## Slide 41: Real Stuff: Benchmarking the Intel Core i7
SPEC CPU benchmark
  Workload
    A set of programs run on a computer
    Either the actual collection of applications run by a user or constructed from real programs to approximate such a mix
    Typically specify both the programs and the relative frequencies
  Benchmark
    Programs specifically chosen to measure performance
    To predict the performance of the actual workload
    To know accurately “which case is common”
  SPEC (system performance evaluation corporation) benchmark
    Standard sets of benchmarks for modern computer systems
    Funded and supported by a number of computer vendors
    SPEC CPU2006 (CINT2006 + CFP2006)
      The latest benchmark set focusing on processor performance

## Slide 42
SPEC CPU benchmark (Cont.)
  SPEC (system performance evaluation corporation) benchmark (Cont.)
    Reported measurement
      SPEC ratio: normalized execution time
        To divide the execution time of a reference processor by the execution time of the measured computer
        The inverse of execution time
      Summary measurement
        Geometric mean of the SPEC ratios to all benchmarks
Fig. 1.18 SPECINT2006 benchmarks running on a 2.66 GHz Intel Core i7 920.

## Slide 43
SPEC power benchmark
  To report power consumption of servers at different workload levels over a period time
    Divided into 10% increments
  Performance is measured in throughput
    Unit: business operations per second (ssj_ops)
    Summary measurement
Fig. 1.19 SPECpower_ssj2008 running on a dual socket 2.66 GHz Intel Xeon X5650 with 16 GB of DRAM and one 100 GB SSD disk.

## Slide 44: Fallacies and Pitfalls
Pitfalls
  Expecting the improvement of one aspect of a computer to increase performance by an amount proportional to the size of the improvement
    Example
      Problem
        A program runs in 100 seconds, with multiplication responsible for 80 seconds
        If we want the program to run five times faster, how much do we have to improve the speed of multiplication?
      Solution
        Execution time after improvement =
        Execution time after improvement = 80 sec / n + (100 – 80 sec)
         20 sec = 80 sec / n + 20 sec  0 = 80 sec / n !!
    Amdahl’s law
      A rule stating that the performance enhancement possible with a given improvements is limited by the amount that the improved feature is used

## Slide 45
Pitfalls (Cont.)
  Using a subset of the performance equation as a performance metric
    Nearly all alternatives to the use of time as the performance metric have led to misleading claims, distorted results, or incorrect interpretations
    MIPS (million instructions per second)
      Instruction execution rate
      To specify performance inversely to execution time
    Problems with using MIPS as a measure
      Cannot compare computers with different instruction sets
        MIPS does not take into account the capabilities of the instructions
      A computer cannot have a single MIPS rating
        MIPS varies between programs on the same computer
      MIPS can vary inversely with performance
    Example
      Problem
        Computers clock rate: 4 GHz
        Which code sequence will execute faster according to MIPS? According to execution time?

## Slide 46
Pitfalls (Cont.)
  Using a subset of the performance equation as a performance metric (Cont.)
    Example (Cont.)
      Solution
        CPU clock cycles1 = (5  1 + 1  2 + 1  3)  109 = 10  109
        CPU clock cycles2 = (10  1 + 1  2 + 1  3)  109 = 15  109
        faster !
        faster !
 | CPI for each instruction class |  | 
 | A | B | C
CPI | 1 | 2 | 3
 | Instruction counts (in billions) for each instruction class |  | 
 | A | B | C
Compiler 1 | 5 | 1 | 1
Compiler 2 | 10 | 1 | 1

## Slide 47
Fallacies
  Computers at low utilization use little power
    Utilization of servers in Google’s WSC
      Mostly operates at 10%~50% of the load
      At 100% of the load less than 1% of the time
      The specially configured computer in 2012 still uses 33% of the peak power at 10% of the load
    To redesign hardware to achieve energy-proportional computing
  Designing for performance and designing for energy efficiency are unrelated goals
    Energy = power  time
    Hardware or software optimizations that take less time save energy overall even if the optimization takes a bit more energy when it is used
Fig. Extra SPECPower results for three servers with the best overall ssj_ops per watt in the fourth quarter of 2007.
Server Manufacturer | Micro-processor | Total Cores/ Sockets | Clock Rate | Peak Performance (ssj_ops) | 100% Load Power | 50% Load Power | 50% Load/ 100% Power | 10% Load Power | 10% Load/ 100% Power | Active Idle Power | Active Idle/ 100% Power
HP | Xeon E5440 | 8/2 | 3.0 GHz | 308,022 | 269 W | 227 W | 84% | 174 W | 65% | 160 W | 59%
Dell | Xeon E5440 | 8/2 | 2.8 GHz | 305,413 | 276 W | 230 W | 83% | 173 W | 63% | 157 W | 57%
Fujitsu Seimens | Xeon X3220 | 4/1 | 2.4 GHz | 143,742 | 132 W | 110 W | 83% | 85 W | 65% | 80 W | 60%