## Slide 1: Arithmetic for Computers

## Slide 2: Outline
Fixed-Point Numbers
Addition and Subtraction
Multiplication
Division
Floating Point
Fallacies and Pitfalls

## Slide 3: Fixed-Point Numbers
Preliminary
  In a fixed-point number system, each number has exactly the same number of digits, and the point is always in the same place
    0.23, 5.12, 9.11
    Ordinary integers: 2, 53, 120
    (11.10)2, (01.10)2, (00.11)2
  In the computer the binary point is not stored anywhere
Range and precision in fixed-point numbers
  A fixed-point representation can be characterized by
    Range of expressible numbers
      The distance between the largest and smallest numbers
    Precision
      The distance between two adjacent numbers on a number line
    Error
      ½ of the difference between two adjoining numbers

## Slide 4
Range and precision in fixed-point numbers (Cont.)
  Example
    Three digits, the decimal point is placed two digits from the right
    Range: [0.00, 9.99] Precision: 0.01 Error: 0.005
  There is a trade-off between range and precision if the total number of digits is limited
  There is no reason why the range must begin with 0
The associative law of algebra does not always hold in computers
  Associative law of algebra: a + (b + c) = (a + b) + c
  Example
    Range: [-9, 9] (a, b, c) = (7, 4, -3)
    a + (b + c) = 7 + (4 + -3) = 8
    (a + b) + c = (7 + 4) + -3 = 11 + -3 11 is outside the range
  To detect overflow wherever it occurs

## Slide 5
Radix number systems
  The base or radix of a number system defines the range of possible values that a digit may have
    Binary (base 2)
    Octal (base 8): one octal digit is represented by 3 binary bits
    Hexadecimal (base 16): one hexadecimal digit is represented by 4 binary bits
  The general form for determining the decimal value of a number in a radix k fixed-point number system
    Weighted position code
    Ex: (541.25)10 = 5  102 + 4  101 + 1  100 + 2  10-1 + 5  10-2
    = (500)10 + (40)10 + (1)10 + (2/10)10 + (5/100)10
    Ex: (1010.01)2 = 1  23 + 0  22 + 1  21 + 0  20 + 0  2-1 + 1  2-2
    = (8)10 + (0)10 + (2)10 + (0)10 + (0/2)10 + (1/4)10
  Most Significant Bit (MSB) vs. Least Significant Bit (LSB)
    MSB: the leftmost bit
    LSB: the rightmost bit

## Slide 6
Conversions among radices
  Converting the integer part of a fixed-point number: the remainder method
    Description
      General polynomial form for representing a binary integer:
      bi  2i + bi-1  2i-1 + ... + b1  21 + b0  20
      To divide the integer by 2:
      bi  2i-1 + bi-1  2i-2 + ... + b1  20 remainder: b0
      All bi can be obtained by iterating the process on the remaining polynomial
    Example
Fig. Extra.1 A conversion from a base 10 integer to a base 2 integer using the remainder method.

## Slide 7
Conversions among radices (Cont.)
  Converting the fractional part of a fixed-point number: the multiplication method
    Description
      General polynomial form for representing a binary fraction:
      b-1  2-1 + b-2  2-2 + b-3  2-3 + …
      To multiply the integer by 2:
      b-1 + b-2  2-1 + b-3  2-2 + …
      All bi can be obtained by iterating the process on the remaining fraction
    Example
Fig. Extra.2 A conversion from a base 10 fraction to a base 2 fraction using the multiplication method.

## Slide 8
Conversions among radices (Cont.)
  Non-terminating fractions
    Not all terminating base 10 fractions have a terminating base 2 form
    Description
      A non-repeating fraction in base b can be represented as i / bk for some integers i and k
      A non-repeating base 10 fraction:
      i/10k = i/(5k  2k) = j/2k where j = i/5k
      Hence, if a non-repeating base 10 fraction has a non-repeating base 2 form, 5k must be a factor of i
Fig. Extra.3 A terminating base 10 fraction that does not have a terminating base 2 form.

## Slide 9
Conversions among radices (Cont.)
  Binary, octal, and hexadecimal radix representations
    k bits are needed to represent each digit in base 2k
    Base 10 form can be used as an intermediate step when we perform an unnatural conversion
Fig. Extra.4 Values for digits in the binary, octal, decimal, and hexadecimal number systems.

## Slide 10
An early look at computer arithmetic
Fig. Extra.5 Example of binary addition.

## Slide 11
Signed fixed-point numbers
  For a k-bit number, there are 2k possible bit patterns
    One half of the bit patterns to positive numbers and the other half to negative numbers
    Four commonly used signed representations
Table Extra.1 3-bit integer representations.

## Slide 12
Signed fixed-point numbers (Cont.)
  Signed magnitude (sign and magnitude)
    The leftmost bit is used for the sign (0 for positive, 1 for negative)
      (+12)10 = (00001100)2 (-12)10 = (10001100)2
      +0 = (00000000)2 -0 = (10000000)2
    For a k-bit number
      Range: [-(2k-1 – 1), 2k-1 – 1]
      2k – 1 different numbers can be represented
  One’s complement
    0  1 (complementing)
      (+12)10 = (00001100)2 (-12)10 = (11110011)2
      +0 = (00000000)2 -0 = (11111111)2
      The leftmost bit is the sign bit (0 for positive, 1 for negative)
    For a k-bit number
      Range: [-(2k-1 – 1), 2k-1 – 1]
      2k – 1 different numbers can be represented
    Not commonly used in arithmetic calculations
    Practical application
      Checksums in the headers of network packets

## Slide 13
Signed fixed-point numbers (Cont.)
  Two’s complement
    0  1 then add 1, discard the carry-out from the MSB
      (+12)10 = (00001100)2 (-12)10 = (11110100)2
      +0 = (00000000)2 -0 = (00000000)2
      The leftmost bit is the sign bit (0 for positive, 1 for negative)
    For a k-bit number
      Range: [-2k-1, 2k-1 – 1]
      2k different numbers can be represented
    The most commonly used representation in conventional computers
  Excess (biased) representation
    Two’s complement form plus a bias (Ex: excess 128)
      (+12)10 = (10001100)2 (-12)10 = (01110100)2
      (-128)10 = (00000000)2 (+127)10 = (11111111)2
      +0 = (10000000)2 -0 = (10000000)2
      The leftmost bit is the sign bit (1 for positive, 0 for negative)
      Numerically smaller numbers have smaller bit patterns
    For a k-bit number
      Range: [-2k-1, 2k-1 – 1]
      2k different numbers can be represented

## Slide 14
Sign extension
  A number is placed into a larger container
    To pad the left side with 0s
      Positive number: correct
      Negative number: incorrect
    To copy the sign bit to the left side: sign extension

## Slide 15
Sign extension (Cont.)
  A number is placed into a smaller container
    To remove bits on the left side

## Slide 16: Addition and Subtraction
Binary addition and subtraction
  Digits are added bit by bit from right to left, with carries passed to the next digit to the left
  Subtraction uses addition, but the appropriate operand is negated before being added
  Example: adding and then subtracting 6ten to 7ten in binary
    Addition
    Subtraction

## Slide 17
Overflow
  To occur when the result from an operation cannot be represented with the available hardware
  Examples
    The carry-out of the leftmost bit is discarded because the number system is modular
    Examples without overflow
    Example with overflow
      01010000 (+80)10
      + 00110010 (+50)10
      --------------------------------
      10000010 (-126)10

## Slide 18
Overflow (Cont.)
  When overflow cannot occur
    No overflow can occur when adding positive and negative operands
      The sum must be no larger than one of the operands
    No overflow can occur when subtracting two operands of the same sign
      Can be ended up by adding operands of different signs
  How to detect overflow for two’s complement numbers in a computer
    If the numbers being added are of the same sign and the result is of the opposite sign, then an overflow occurs
    If the numbers being added are of opposite signs, then an overflow will never occur
    If a positive (negative) number is subtracted from a negative (positive) number and the result is positive (negative), then an overflow occurs
    If the numbers being subtracted are of the same sign, then an overflow will never occur
Fig. 3.2 Overflow conditions for addition and subtraction.

## Slide 19: Multiplication
Unsigned multiplication
  Review the multiplication of decimal numbers in longhand
    Multiplicand  Multiplier = Product
    Example: 100010  100110 (using only digits 0 and 1)
    Steps
      To take the digits of the multiplier one at a time from right to left
      To multiply the multiplicand by the single digit of the multiplier
        Just place a copy of the multiplicand in the proper place if the multiplier digit is a 1
        Place 0 in the proper place if the digit is 0
      To shift the intermediate product one digit to the left of the earlier intermediate products
    The number of digits in the product
      n-bit multiplicand  m-bit multiplier = (n+m)-bit product
      (ignoring the sign bits)
      We frequently want a 32-bit product as the result of
      multiplying two 32-bit numbers
       Must copy with overflow

## Slide 20
Unsigned multiplication (Cont.)
  Sequential version of the multiplication algorithm and hardware
    First version of the multiplication hardware
      Multiplier is in the 32-bit Multiplier register
      The 64-bit Product register is initialized to 0
      A 64-bit Multiplicand register is initialized with the 32-bit multiplicand in the right half and zero in the left half
      The Multiplier register is shifted right 1 bit each step
      The Multiplicand register is shifted left 1 bit each step to align the multiplicand with the sum being accumulated in the 64-bit Product register
Fig. 3.3 First version of the multiplication hardware.

## Slide 21
Unsigned multiplication (Cont.)
  Sequential version of the multiplication algorithm and hardware (Cont.)
    Three basic steps needed for each bit
      Step 1: the LSB of the multiplier determines whether the multiplicand is added to the Product register
      Step 2: the left shift of the Multiplicand register has the effect of moving the intermediate operands to the left
      Step 3: the shift right of the Multiplier register gives the next bit of the multiplier to examine in the following iteration
      Above steps are repeated 32 times
Fig. 3.4 The first multiplication algorithm, using the hardware shown in Fig. 3.3.

## Slide 22
Unsigned multiplication (Cont.)
  Sequential version of the multiplication algorithm and hardware (Cont.)
    Above three steps are repeated 32 times to obtain the product
      If each step took a clock cycle, this algorithm requires almost 100 clock cycles to multiply two 32-bit numbers
    Refined version of the multiplication hardware
      To perform operations in parallel: 1 clock cycle per step
        The multiplier and multiplicand are shifted while the multiplicand is added to the product if the multiplier bit is a 1
        The hardware has to ensure that it tests the LSB of the multiplier and gets the pre-shifted version of the multiplicand
      To halve the width of the adder and registers
        The multiplier is placed in the right half of the Product register
        The Product is shifted right
Fig. 3.5 Refined version of the multiplication hardware.

## Slide 23
Unsigned multiplication (Cont.)
  Sequential version of the multiplication algorithm and hardware (Cont.)
    Example: a multiply algorithm
      Using 4-bit numbers to save space, multiply 210  310, or 00102  00112
      Using the hardware in Fig. 3.3 and algorithm in Fig. 3.4
Fig. 3.6 Multiply example using algorithm in Fig. 3.4.

## Slide 24
Signed multiplication
  Leaving the signs out of the calculation
    To convert the multiplier and multiplicand to positive numbers and then remember the original signs
    The algorithms should be run for 31 iterations
  The algorithm in Fig. 3.4 will work for signed numbers
    The shifting steps would need to extend the sign of the product
    When the algorithm completes, the lower word would have the 32-bit product
Iteration | Step | Multiplier | Multiplicand | Product
0 | Initial values | 1101 | 0000 0010 | 0000 0000
1 | 1a: 1  Prod = Prod + Mcand | 1101 | 0000 0010 | 0000 0010
 | 2: Shift left Multiplicand | 1101 | 0000 0100 | 0000 0010
 | 3: Shift right Multiplier | 1110 | 0000 0100 | 0000 0010
2 | 1: 0  No operation | 1110 | 0000 0100 | 0000 0010
 | 2: Shift left Multiplicand | 1110 | 0000 1000 | 0000 0010
 | 3: Shift right Multiplier | 1111 | 0000 1000 | 0000 0010
3 | 1a: 1  Prod = Prod + Mcand | 1111 | 0000 1000 | 0000 1010
 | 2: Shift left Multiplicand | 1111 | 0001 0000 | 0000 1010
 | 3: Shift right Multiplier | 1111 | 0001 0000 | 0000 1010
4 | 1a: 1  Prod = Prod + Mcand | 1111 | 0001 0000 | 0001 1010
 | 2: Shift left Multiplicand | 1111 | 0010 0000 | 0001 1010
 | 3: Shift right Multiplier | 1111 | 0010 0000 | 0001 1010
210  (-3)10 = -610
00102  11012 = 10102

## Slide 25
Faster multiplication
  Whether the multiplicand is to be added or not is known at the beginning of the multiplication by looking at each of the 32 multiplier bits
  To provide one 32-bit adder for each bit of the multiplier
    Two input bits
      One input is the multiplicand ANDed with a multiplier bit
      One input is the output of a prior adder
    To organize these 32 additions
      To connect the outputs of adders on the right to the inputs of adders on the left
      Parallel tree
Fig. 3.7 Fast multiplication hardware.

## Slide 26: Division
Unsigned division
  Review the division of decimal numbers in longhand
    Dividend / Divisor = Quotient + Remainder
    Dividend = Quotient  Divisor + Remainder
    Example: 100101010 / 100010 (using only digits 0 and 1)
    Steps
      To see how big a number can be subtracted
      To create a digit of the quotient on each attempt

## Slide 27
Unsigned division (Cont.)
  A division algorithm and hardware
    First version of the division hardware
      The 32-bit Quotient register is initialized to 0
      The divisor is placed in the left half of the 64-bit Divisor register
      The Remainder register is initialized with the dividend (sign extension)
      The Divisor register is shifted right 1 bit each step to align with the dividend
      The Quotient register is shifted left 1 bit each step
Fig. 3.8 First version of the division hardware.

## Slide 28
Unsigned division (Cont.)
  A division algorithm and hardware (Cont.)
    Three steps of the first division algorithm
      Step 1: subtract the Divisor register from the Remainder register
      Step 2a: if the result is positive, we generate a 1 in the quotient
      Step 2b: if the result is negative, we restore the original value to the remainder and generate a 0 in the quotient
      Step 3: the Divisor register is shifted right 1 bit
      Above steps are repeated 33 times
Fig. 3.9 A division algorithm, using the hardware in Fig. 3.8.

## Slide 29
Unsigned division (Cont.)
  A division algorithm and hardware (Cont.)
    Example: a divide algorithm
      Using 4-bit numbers to save space, divide 710 / 210, or 0000 01112 / 00102
      Using the hardware in Fig. 3.8 and algorithm in Fig. 3.9
Fig. 3.10 Division example using the algorithm in Fig. 3.9.

## Slide 30
Unsigned division (Cont.)
  A division algorithm and hardware (Cont.)
    An improved version of the division hardware
      To shift the operands and the quotient simultaneously with the subtraction
      To halve the width of the adder and registers
        The Remainder register is shifted left
        To combine the Quotient register with the right half of the Remainder register
Fig. 3.11 An improved version of the division hardware.

## Slide 31
Signed division
  To remember the signs of the divisor and dividend and then negate the quotient if the signs disagree
  Dividend = Quotient  Divisor + Remainder
  The dividend and remainder must have the same signs
    +7  -2: Quotient = -3, Remainder = +1
    -7  -2: Quotient = +3, Remainder = -1
Faster division: SRT division
  Try to predict several quotient bits per step
    Using a table lookup based on the upper bits of the dividend and remainder
      6 bits from the remainder and 4 bits from the divisor to index a table
    Subsequent steps to correct wrong predictions
    A typical value today is 4 bits
  The accuracy depends on having proper values in the lookup table

## Slide 32: Floating Point
Preliminary
  Programming languages support numbers with fractions
  Floating point
    Computer arithmetic that represent numbers in which the decimal point (or binary point) is not fixed
  Scientific notation
    Numbers with a single digit to the left of the decimal point
    Example
      1.010  10-9, 3.155710  109
      1.02  2-1
  Normalized
    A number in floating-point notation that has no leading 0s
    Example
      1.010  10-9 = 0.110  10-8 = 10.010  10-10 1.010  10-9 is in normalized form
      1.xxxxxxxxx2  2yyyy

## Slide 33
Floating-point representation
  General form of a floating-number: (-1)s  F  2E
    s is the sign of the floating-point number
    F: fraction (mantissa)
      A value generally between 0 and 1 to determine the precision
      Larger F enhances the precision of the fraction
    E: exponent
      A signed integer to determine the range
      Larger E increases the range of numbers that can be represented
    A tradeoff is between precision and range
  Floating-point representation in MIPS
    Format (single precision)
      A floating-point value represented in a single 32-bit word
      A separate sign bit: 0 or positive, 1 for negative
      8-bit exponent field (including the sign of the exponent)
      23-bit fraction field
      Range: 2.010  10-38 ~ 2.010  1038

## Slide 34
Floating-point representation (Cont.)
  Floating-point representation in MIPS (Cont.)
    Overflow
      A positive exponent is too large to be represented in the exponent field
    Underflow
      A negative exponent is too large to fit in the exponent field
    Format (double precision)
      A floating-point value represented in two 32-bit words
      Sign bit, 11-bit exponent field, 52-bit fraction field
      Range: 2.010  10-308 ~ 2.010  10308
      Greater precision due to the much larger fraction

## Slide 35
Floating-point representation (Cont.)
  IEEE 754 floating-point standard
    Making the leading 1-bit of normalized binary numbers implicit
      The significand is actually 24-bit long in single precision and 53-bit long in double precision
      Since 0 has no leading 1, it needs a special format to represent
    Format
      00…002 represent 0
      The representation of floating-point number
        (-1)s  (1 + Fraction)  2(Exponent – Bias)
        Using a bias of 127 for single precision and 1023 for double precision
        Range of single precision number
        1.00000000000000000000000  2-126 ~ 1.11111111111111111111111  2+127
      The largest exponent is reserved for infinity and NaN (not a number)
        infinity (+ and -) can represent the result of a divide by 0
        NaN can represent invalid operations, such as 0/0 or subtracting infinity from infinity

## Slide 36
Floating-point representation (Cont.)
  IEEE 754 floating-point standard (Cont.)
    Format (Cont.)
      The representation of denormalized number
        Without the leading 1-bit
        (-1)s  Fraction  2-126 in single precision and (-1)s  Fraction  2-1022 in double precision
        To represent numbers between 0 and the smallest (or largest) positive (or negative) number in the floating-point number type
    Example: show the IEEE 754 binary representation of the number -0.7510
      -0.7510 = (-3/4)10 = (-3/22)10 = -0.112
      Scientific notation: -0.112  20 Normalized form: -1.12  2-1
      The general form of single precision: (-1)s  (1 + Fraction)  2(Exponent – 127)
       -1.12  2-1 = (-1)1  (1 + .1000 0000 0000 0000 0000 0002)  2(126 – 127)

## Slide 37
Floating-point representation (Cont.)
  IEEE 754 floating-point standard (Cont.)
    Example: converting binary to decimal floating point
      Sign bit: 1 Exponent field: 129 Fraction field: 1  2-2 = 1/4 = 0.25
      (-1)s  (1 + Fraction)  2(Exponent – Bias) = (-1)1  (1 + 0.25)  2(129 – 127)
      = -1  1.25  22 = -1.25  4 = -5.0

## Slide 38
IEEE 754 floating-point standard
  分 5 種 types, exponent 若為全 0 或全 1 代表特殊 type
    Exponent 全 0 或全 1 不代表真正的 exponent 值
  為何需要 denormalized number
    IEEE 754 有使用 hidden bit, 因此能表示的最小 positive floating-point number 為
    0 0000 0001 0000 0000 0000 0000 0000 000
    + -126 1.00…0  20  2-126 = 2-126
    若將所有能表示的 floating-point number 畫在數線上, 會發現 [0, 2-126] 之間的距離相對很大, 中間的數字都無法表示, 因此設計 denormalized number 希望能表示此區間數字
  如何表示 [0, 2-126] 之間數字
    這些數字可表示為 a  2-126, a < 1
    配合 IEEE 754 standard 原本的格式可以下列方式表示
      Exponent 固定為 -126
      Mantissa 不使用 hidden bit, 意即 mantissa 表示的數字小於 1

## Slide 39
Floating-point addition
  Example: 9.99910  101 + 1.61010  10-1
    Assume we can store 4 decimal digits of the significand and 2 decimal digits of the exponent
    Step 1: align the decimal point of the number that has the smaller exponent
      1.61010  10-1 = 0.161010  100 = 0.0161010  101
      We can represent only 4 decimal digits  0.01610  101
      The number will be truncated directly
    Step 2: add the significands
      9.99910 + 0.01610 = 10.01510
      The sum is 10.01510  101
    Step 3: adjust the sum to normalized form
      10.01510  101 = 1.001510  102
      Check for overflow or underflow to make sure the exponent still fits in its field
    Step 4: round the number
      Truncate the number: if the digit to the right of the desired point is between 0 and 4
      Add 1 to the digit: if the number to the right is between 5 and 9
      1.001510  102  1.00210  102
      If the sum is no longer normalized  perform step 3 again

## Slide 40
Floating-point addition (Cont.)
  The algorithm for binary floating-point addition
    Step 1: adjust the significand of the number with the smaller exponent
      Shift the smaller number to the right until its exponent would match the larger exponent
    Step 2: add the two significands
    Step 3: normalize the results and check for overflow or underflow
      Depend on the precision of the operands
      The patterns of all 0 and all 1 bits in the exponent are reserved
      For single precision, the exponent is between -126 and 127
    Step 4: round the significand to the appropriate number of bits
      Perform step 3 again if necessary
Fig. 3.14 Floating-point addition.

## Slide 41
Floating-point addition (Cont.)
  Example: try to add 0.510 and -0.437510 in binary
    Assume that we keep 4 bits of precision
    The binary version of the two numbers in normalized form
      0.510 = (1/2)10 = (1/21)10 = 0.12 = 0.12  20 = 1.0002  2-1
      -0.437510 = (-7/16)10 = (-7/24)10 = -0.01112 = -0.01112  20 = -1.1102  2-2
    Step 1: shift the significand of the number with the smaller exponent
      -1.1102  2-2 = -0.1112  2-1
    Step 2: add the significands
      1.0002  2-1 + (-0.1112  2-1) = 0.0012  2-1
    Step 3: normalized the sum and check for overflow or underflow
      0.0012  2-1 = 0.0102  2-2 = 0.1002  2-3 = 1.0002  2-4
      Since -126  -4  127, there is no overflow or underflow
      The biased exponent: -4 + 127 = 123, which is between 1 and 254
    Step 4: round the sum
      The sum 1.0002  2-4 already fits exactly in 4 bits, so there is no change to the bits du to rounding
    1.0002  2-4 = 0.00010002 = 0.00012 = (1/24)10 = (1/16)10 = 0.062510

## Slide 42
Fig. 3.15 Block diagram of an arithmetic unit dedicated to floating-point addition.

## Slide 43
Floating-point multiplication
  Example: 1.11010  1010  9.20010  10-5
    Assume we can store 4 decimal digits of the significand and 2 decimal digits of the exponent
    Step 1: calculate the exponent of the product by simply adding the exponents of the operands together
      New exponent = 10 + (-5) = 5
      The biased exponents: (10 + 127) + (-5 + 127) – 127 = 132 = 5 + 127
    Step 2: multiply the significands
      There should be 6 digits from the right in the product significand
      We can keep only 3 digits to the right of the decimal point
      10.21200010 = 10.21210  105
    Step 3: normalize the product and check for overflow and underflow
      10.21210  105 = 1.021210  106
    Step 4: round the number
      1.021210  106 = 1.02110  106
    Step 5: determine the sign of the product
      Depend on the signs of the original operands
      +1.02110  106

## Slide 44
Floating-point multiplication (Cont.)
  The algorithm for binary floating-point multiplication
    Step 1: calculate the new exponent of the product
      Add the biased exponents and subtract one bias
    Step 2: multiply the significands
    Step 3: normalize the product and check for overflow or underflow
      Optional
      The size of the exponent is checked for overflow or underflow
    Step 4: round the product
      If rounding leads to further normalized, we once again check for exponent size
    Step 5: determine the sign bit
Fig. 3.16 Floating-point multiplication.

## Slide 45
Floating-point multiplication (Cont.)
  Example: try to multiply 0.510 and -0.437510 in binary
    Assume that we keep 4 bits of precision
    The binary version of the two numbers in normalized form
      0.510 = 1.0002  2-1 -0.437510 = -1.1102  2-2
    Step 1: calculate the new exponent of the product
      (-1 + 127) + (-2 + 127) – 127 = 124 = -3 + 127 or (-1) + (-2) = -3
    Step 2: multiply the significands
      We need to keep it to 4 bits
      11100002 = 1.1100002  2-3 = 1.1102  2-3
    Step 3: normalize the product and check for overflow or underflow
      Since -126  -3  127, there is no overflow or underflow
      The biased exponent: -3 + 127 = 124, which is between 1 and 254
    Step 4: round the product
      The sum 1.1102  2-3 already fits exactly in 4 bits, so there is no change to the bits du to rounding
    Step 5: determine the sign bit
      Since the signs of the original operands differ  -1.1102  2-3
    -1.1102  2-3 = -0.0011102 = -0.001112 = -(7/25)10 = -(7/32)10 = -0.2187510

## Slide 46
Accurate arithmetic
  Floating-point numbers are normally approximations for a number they can’t really represent
    The computer numbers have limited size and hence limited precision
    Getting the floating-point representation close to the actual number
  It requires extra bits in the calculation to round accurately
    If every intermediate result had to be truncated to the exact number of digits, there would be no opportunity to round
    IEEE 754 always keeps two extra bits on the right during intermediate additions
      Guard bit and round bit
  Example: 2.5610  100 + 2.3410  102
    Round to the nearest decimal number with 3 significant decimal digits
    With guard and round digits
      2.5610  100 + 2.3410  102 = (0.025610 + 2.340010)  102 = 2.365610  102
      We have two digits to round  2.3710  102
        0 ~ 49 to round down, 51~99 to round up, 50 is the tiebreaker
    Without guard and round digits
      To drop two digits from the calculation
      2.5610  100 + 2.3410  102 = (0.0210 + 2.3410)  102 = 2.3610  102

## Slide 47
Accurate arithmetic (Cont.)
  IEEE 754 has four rounding modes
    Always round up (toward +), always round down (toward -), truncate
    Round to nearest even: the most commonly used
      To determine what to do if the number is exactly halfway in between
      If the LSB retained in a halfway case is odd  add 1
      If the LSB retained in a halfway case is even  truncate
      Always creates a 0 in the LSB in the tie-breaking case
      Ex: 1.0110102  1.01102 (truncate) 1.0111102  1.10002 (add 1)
  Sticky bit
    A bit used in rounding in addition to grand and round bits
    Sticky bit is set whenever there are nonzero bits to the right of the round bit
    Example: 5.0110  10-1 + 2.3410  102
      Round to the nearest decimal number with 3 significant decimal digits
      5.0110  10-1 + 2.3410  102 = (0.005010 + 2.340010)  102 = 2.345010  102
        The sticky bit is set since there are nonzero bits to the right
      With the sticky bit to remember that the number is actually larger than 2.345010
       Round to 2.3510  102
      Without the sticky bit  Round to 2.3410  102

## Slide 48: Fallacies and Pitfalls
Fallacies
  Just as a left shift instruction can replace an integer multiply by a power of 2, a right shift is the same as an integer division by a power of 2
    Above statement is only true for unsigned integers
    The problem for signed integer
      To divide -510 by 410  the quotient should be -110
      -510 = 1111 1111 1111 1111 1111 1111 1111 10112
      Shifting right by two: 0011 1111 1111 1111 1111 1111 1111 11102  -110
    Solution: to have an arithmetic right shift that extends the sign bit instead of shifting in 0s
      -510 = 1111 1111 1111 1111 1111 1111 1111 10112
      2-bit arithmetic right: 1111 1111 1111 1111 1111 1111 1111 11102 = -210  -110
  Parallel execution strategies that work for integer data types also work for floating-point data types
    Read it yourself

## Slide 49
Fallacies (Cont.)
  Only theoretical mathematicians care about floating-point accuracy
Fig. 3.25 A sampling of newspaper and magazine articles from November 1994, including the New York Times, San Jose Mercury News, San Francisco Chronicle, and Infoworld.

## Slide 50
Pitfalls
  Floating-point addition is not associative
    Associativity holds for a sequence of 2’s complement integer additions, even if the computation overflows
    Associativity does not hold for floating-point numbers because
      Floating-point numbers are approximations of real numbers
      Computer arithmetic has limited precision
    Problems occur when adding two large numbers of opposite signs plus a small number
    Example
      a = 1.510  1038 b = 1.010 c = -1.510  1038
      c + (a + b) = -1.510  1038 + (1.510  1038 + 1.010)
      = -1.510  1038 + (1.510  1038) = 0.010
      (c + a) + b = (-1.510  1038 + 1.510  1038) + 1.010
      = 0.010 + 1.010 = 1.010
      c + (a + b)  (c + a) + b
  The MIPS instruction add immediate unsigned (addiu) sign-extends its 16-bit immediate field
    Read it yourself