## Slide 1: Large and Fast: Exploiting Memory Hierarchy

## Slide 2: Outline
Introduction
Memory Technologies
The Basics of Caches
Measuring and Improving Cache Performance
Dependable Memory Hierarchy
Virtual Memory
A Common Framework for Memory Hierarchies
Using a Finite-State Machine to Control a Simple Cache
Real Stuff: The ARM Cortex-A8 and Intel Core i7 Memory Hierarchies
Fallacies and Pitfalls

## Slide 3: Introduction
A library example
Principle of locality
  Programs access a relatively small portion of their address space at any instant of time
  It is impossible to make most memory accesses fast and still have large memory in computers
  Temporal locality (locality in time)
    If an item is referenced, it will tend to be reference again soon
    Ex: loops
  Spatial locality (locality in space)
    If an item is reference, items whose addresses are close by will tend to be referenced soon
    Ex: program (instructions) and array data are normally sequentially accessed

## Slide 4
Memory hierarchy
  The basic structure
    Multiple levels of memory with different speeds and sizes
    The faster memories are more expensive per bit than the slower memories and thus are smaller
    The faster memory is close to the processor and the slower, less expensive memory is below it
      To present the user with as much memory as is available in the cheapest technology
      To provide access at the speed offered by the fastest memory
    The data is similarly hierarchical
      All the data is stored at the lowest level
      Inclusion property
        A level closer to the processor is
      generally a subset of any level
      further away
Fig. 5.1 The basic structure of a memory hierarchy.

## Slide 5
Memory hierarchy (Cont.)
  Data is copied between only two adjacent levels at a time
    The upper level is smaller, faster, and expensive
    Block (line)
      The minimum unit of information that can be either present or not present in a cache
    Hit vs. Miss
      Hit: the data requested by the processor appears in some block in the upper level
      Miss: the requested data is not found in the upper level
    Hit rate (hit ratio) vs. Miss rate
      The fraction of memory accesses found (or not found) in the upper level
      Hit rate + Miss rate = 1
    Hit time
      The time to access the upper level of the memory hierarchy
      Including the time needed to determine whether the access
      is a hit or a miss
    Miss penalty
      The time to replace a block in the upper level
      Including the time to deliver this block to the processor
    Hit time will be much smaller than the time to access the
    next level in the hierarchy

## Slide 6
Memory systems are critical to performance
  All programs spend much of their time accessing memory
  The memory system is necessarily a major factor in determining performance
Memory hierarchy vs. locality
  Programs exhibit both temporal locality and spatial locality
    Temporal locality
      To keep more recently accessed data items closer to the processor
      Accesses that hit in the highest level of the hierarchy can be processed quickly
    Spatial locality
      To move blocks consisting of multiple contiguous words in memory to upper levels of the hierarchy
  In most system, data cannot be present in
  level i unless it is also present in level i + 1
Fig. 5.3 This diagram shows the structure of a memory hierarchy: as the distance from the processor increases, so does the size.

## Slide 7: Memory Technologies
Preliminary
  Four primary technologies used today in memory hierarchies
    DRAM (dynamic random access memory)
      Used to implement the main memory
      Slower and less costly per bit than SRAM
      DRAM uses significantly less area per bit of memory
    SRAM (static random access memory)
      Used to implement the cache
    Flash memory
      Nonvolatile memory, the secondary memory in PMD (personal mobile devices)
    Magnetic disk
      Used to implement the largest and slowest level in the hierarchy in servers
  The access time and price per bit vary widely among these technologies

## Slide 8
SRAM technology
  Memory arrays with (usually) a single access port that can provide either a read or a write
    A fixed access time to any datum
    The read and write access times may differ
  SRAMs don’t need to refresh
    The access time is very close to the cycle time
      Access time: the time between a read is requested and the desired word arrive
      Cycle time: the minimum time between requests to memory
      Cycle time is greater than access time
    Typically uses 6~8 transistors per bit to prevent the information from being disturbed when read
    SRAM needs only minimal power to retain the charge in standby mode
  Today all levels of caches are integrated onto the processor chip
DRAM technology
  In a DRAM, the value kept in a cell is stored as a charge in a capacitor
    A single transistor is used to access the stored charge
    DRAM is much denser and cheaper per bit than SRAM

## Slide 9
DRAM technology (Cont.)
  DRAM cells must be periodically refreshed
    To read contents for a cell and write it back
      The charge can be kept for several milliseconds
      The difference between the access time and the cycle time as well as the need to refresh
      Designers try to keep time spent refreshing to less than 5% of the total time
    All bits in a row can be refreshed simultaneously
  The internal organization of a DRAM
    The memory is organized as a rectangular matrix addressed by rows and columns
    To multiplex the address lines
      Row address vs. Column address
      Row access strobe (RAS) vs. Column access strobe (CAS)
    DRAMs buffer rows for repeated access
      Random bits can be accessed in the row buffer until the next row access
      The access time to bits in the row is much lower
      Within the buffer, bits can be transferred by successive addresses or by specifying a block transfer and the starting address
    Making the chip wider also improves the memory bandwidth of the chip

## Slide 10
Fig. extra Internal organization of a 256 Mbit DRAM.
Instead of one 1638416384 memory, a DRAM might use 256 10241024 arrays or 64 20482048 arrays.
Fig. 5.4 Internal organization of a DRAM.

## Slide 11
DRAM technology (Cont.)
  Synchronous DRAM (SDRAM)
    The use of a clock eliminates the time for the memory and processor to synchronize
    Burst mode
      The clock transfers the successive bits in a burst without having to specify additional address bits
    Double data rate (DDR) SDRAM
      Data transfers on both the rising and falling edge of the clock
      Getting twice as much bandwidth
  Multiple banks inside a DRAM
    Each memory bank has its own row buffer
    Address interleaving
      Sending an address to several banks permits them to read or write simultaneously
      Address: bank number, row address, column address
  Dual inline memory modules (DIMMs)
    A DIMM typically contains 4~16 DRAM chips
    DRAM chips are normally organized to be 8 bytes wide for server systems

## Slide 12
Fig. 5.5 DRAM size increased by multiples of four approximately once every three years until 1996, and thereafter considerably slower.

## Slide 13
Flash memory
  A type of electrically erasable programmable read-only memory (EEPROM)
    Nonvolatile memory, more power efficient and shock resistant
    Read time is much shorter than write time
  Wear leveling technique
    Writes can wear out flash memory bits
    To include a controller to remap blocks
      Uniformly distributing written blocks to maximize the lifetime
      PMDs are very unlikely to exceed the write limits in the flash
      To improve yield by mapping out memory cells that were manufactured incorrectly
    To lower the potential performance of flash
Disk memory
  Structure
    A collection of platters
      Covered with magnetic recording material on both sides
      Typically only one or two platters per drive today
      Rotation rate: 5400~15000 RPM Diameter: 2.5 or 3.5 inches
      A movable arm containing a read-write head is located just above each surface

## Slide 14
Disk memory (Cont.)
  Structure (Cont.)
    Each disk surface is divided into concentric circles (tracks)
      Typically tens of thousands of tracks per surface
    Each track is divided into sectors
      Each track may have thousands of sectors
      Sectors are typically 512~4096 bytes in size
    The sequence recorded on the magnetic media
      A sector number, a gap, the information including ECC, a gap, sector number…
    The disk heads for each surface are connected together and move in conjunction
      Every head is over the same track of every surface
      Cylinder: all the tracks under the heads at a given point on all surfaces
Fig. 5.6 A disk showing 10 disk platters and the read-write heads.

## Slide 16
Disk memory (Cont.)
  Three-stage process of the operating system to access data
    Seek time
      Seek: to position the read-write head over the proper track
      Minimum/maximum/average seek time is reported in manuals
      Average seek time depends on the seek distance
        Usually advertised as 3~13 ms
        The actual time may be only 25% ~ 33% of the advertised number
    Rotational latency (rotational delay)
      To wait for the desired sector to rotate under the read-write head
      The average latency is halfway around the disk
      5400~15000 RPM  2.0~5.6 ms
    Transfer time
      To transfer a block of bits
      A function of the sector size, the rotation speed, and the recording density of a track
      Transfer rate is 100~250 MB/sec in 2012
      With a built-in cache: transfer rate is up to 750 MB/sec in 2012

## Slide 17
Disk memory (Cont.)
  The new disk model
    Conventional: sector-track-cylinder model
      Nearby blocks are on the same track
      Blocks in the same cylinder take less time to access (no seek time)
    To offer higher-level intelligent interfaces
      To include a microprocessor inside a disk
      Logical blocks are ordered in serpentine fashion across a single surface
        To capture all the sectors that are recorded at the same bit density
        Sequential blocks may be on different tracks
Primary differences between magnetic disks and semiconductor memory technologies
  Disks have a slower access time because they are mechanical devices
    Flash is 1000 times as fast, DRAM is 100000 times as fast
  Disks are cheaper per bit
    Very high storage capacity at a modest cost
    Disk is 10~100 time cheaper
  Magnetic disks are nonvolatile like flash but no write wear-out problem

## Slide 18: The Basics of Caches
A simple cache
  A safe place to store things that we needed to examine
    The name to represent the level of the memory hierarchy between the processor and main memory
  Two questions to answer
    How do we know if a data item is in the cache?
    If it is, how do we find it?
Fig. 5.7 The cache just before and just after a reference to a word Xn that is not initially in the cache.
Assumption:
The processor requests are each one word and the blocks also consist of a single word

## Slide 19
A simple cache (Cont.)
  Direct-mapped cache
    Each memory location is mapped to exactly one location in the cache
    To assign the cache location based on the memory address of the word
      (block address) modulo (number of cache blocks in the cache)
      It is better to have the number of entries in the cache is a power of 2
      Different memory locations will be mapped to the same cache location
    Tags
      To identify whether a word in the cache corresponds to the requested word
      Only contains the upper portion of the address, which is not used as an index into the cache
    Valid bit
      To indicate whether an entry contains
      a valid address
Fig. 5.8 A direct-mapped cache with eight entries showing the addresses of memory words between 0 and 31 that map to the same cache locations.

## Slide 20
Accessing a cache
  An example: 8-block direct-mapped cache
    Each block contains one word
    The low-order 3 bits of an address give the block number

## Slide 21
Accessing a cache (Cont.)
  A referenced address is divided into
    A cache index
      Used to select the cache block
      The total number of entries in a direct-mapped cache must be a power of 2
    A tag field
      Used to compare with the value of the tag field of the cache
    The least significant 2 bits are ignored when selecting a word in the block
      Words are aligned to multiples of 4 bytes in the MIPS architecture
Fig. 5.7 For this cache, the lower portion of the address is used to select a cache entry consisting of a data word and a tag.

## Slide 22
Accessing a cache (Cont.)
  An example cache: the Intrinsity FastMATH processor
    A embedded microprocessor that uses the MIPS architecture and a simple cache implementation
    Processor
      12-stage pipeline
      When operating at peak speed, both an instruction word and a data word can be request on every clock
    Separate instruction and data caches
      Each is 16 KB (4 K words) with 16-word blocks
      Separate control signals to read and write each cache
      A block index field is used to select the requested word from the 16 words in the indexed block
      To offer both write-through and write-back strategies
      One-entry write buffer
Fig. 5.13 Approximate instruction and data miss rates for the Intrinsity FastMATH processor for SPEC CPU2000 benchmarks.

## Slide 23
Fig. 5.12 The 16 KB caches in the Intrinsity FastMATH each contain 256 blocks with 16 words per block.

## Slide 24
Accessing a cache (Cont.)
  The total number of bits needed for a cache
    Example
      A direct-map cache
      32-bit byte address, 2n blocks with 2m-word block
       Tag size: 32 – (n + m + 2) bits
      Total number of bits: 2n  (block size + tag size + valid field size)
      = 2n  (2m  32 + (32 – n – m – 2) + 1) = 2n  (2m  32 + 31 – n – m)
    Usually to count only the size of the data
  Example: bits in a cache
    Problem
      How many total bits are required for a direct-mapped cache with 16 KB of data and 4-word blocks, assuming a 32-bit address?
    Solution
      16 KB data, 4-word block  210 blocks
      Tag size: 32 – 10 – 2 – 2 = 18 bits
      Each block has 4  32 = 128 bits
      Total cache size = 210  (128 + 18 + 1) = 210  147 = 147 Kbits (or 18.4 KB)
      Total size: 18.4 KB Data size: 16 KB  1.15 times

## Slide 25
Accessing a cache (Cont.)
  Example: mapping an address to a multiword cache block
    Problem
      Consider a cache with 64 blocks and a block size of 16 bytes
      What block number does byte address 1200 map to?
    Solution
      The block is given by: (Block address) modulo (Number of cache blocks)
      The address of the block:
      Block contains all addresses between
      and
      Byte address 1200 is block address
      which maps to cache block number (75 modulo 64) = 11
      Block 11 maps all address between 1200 and 1215

## Slide 26
Accessing a cache (Cont.)
  When the cache block size becomes larger
    Larger blocks exploit spatial locality to lower miss rates
      The miss rate may go up if the block size becomes too large, because the number of blocks that can be held in the cache will become small
    To increase the block size will increase the miss penalty
      Miss penalty: the latency to the first word + the transfer time for the rest of the block
      The transfer time will increase as the block size grows
     To increase the block size and obtain good performance
      To design the memory to transfer larger block more efficiently
Fig. 5.11 Miss rate versus block size.

## Slide 27
Handling cache misses
  When a cache miss occurs
    Done with the processor control unit and a separate controller
    To stall the processor and wait for memory
      To freeze the contents of the temporary and programmer-visible registers
      More sophisticated out-of-order processors can allow execution of instructions while waiting for a cache miss
    To initiate the memory access and refill the cache
  How instruction misses are handled for pipelined datapath
    Send the original PC (current PC – 4) to the memory
    Instruct memory to perform a read and wait for the memory to complete its access
    Write the cache entry
      Putting the data in the data portion of the entry
      Writing the upper bits of the address into the tag field
      Turning the valid bit on
    Restart the instruction execution at the first step (instruction refetch)
  The control of the cache on a data access is essentially identical

## Slide 28
Handling writes
  The cache and memory may be inconsistent
    Data is written into only the data cache without changing memory
  Write-through
    Always write the data into both the memory and the cache
    Simple but not efficient
    Write buffer
      To store the data while it is waiting to be written to memory
      The processor can continue execution after writing the data into the cache and into the write buffer
      A write buffer entry is freed when a write to main memory completes
      If the write buffer is full when the processor reaches a write
        The processor must stall until there is an empty position in the write buffer
        Using deeper write buffer to reduce the occurrence of such stalls
  Write-back
    Data is written only to the block in the cache
    The modified block is written to the memory when it is replaced
    Complex but efficient

## Slide 29
Elaboration
  Write allocate cache vs. No write allocate cache
    For write-through cache
    Write allocate cache
      The missed block is fetched from memory and then allocate a block in the cache
      The appropriate portion of the block in the cache is overwritten
    No write allocate cache
      To update the portion of the block in memory but not put it in the cache
  Combined cache vs. Split cache
    Combined cache
      A single cache stored both instructions and data
      Better hit rate
    Split cache
      Two independent caches that operate in parallel with one handling instructions and one handling data
      Slightly increased miss rate
      Doubling the cache bandwidth
    Almost all processors today use split cache to match what modern pipelines expect

## Slide 30: Measuring and Improving Cache Performance
To measure and analyze cache performance
  To compute the CPU time
    CPU time = (CPU execution clock cycles + Memory-stall clock cycles)
     Clock cycle time
      The costs of cache hits are part of the normal CPU execution cycles
    Memory-stall clock cycles = Read-stall cycles + Write-stall cycles
      (write-through)
        Write-through: with a reasonable write buffer depth, write buffer stall will be small and can be safely ignored
        Write-back: additional stalls arising from the need to write a cache block back to memory when the block is replace

## Slide 31
To measure and analyze cache performance (Cont.)
  To compute the CPU time (Cont.)
      (write-through)
      The read and write miss penalties are the same in most write-through cache organization
      The write buffer stalls are negligible
  Example: calculating cache performance
    Problem
      Instruction cache miss rate: 2%
      Data cache miss rate: 4%
      A processor has a CPI of 2 without any memory stalls
      Miss penalty: 100 cycles for all misses
      Assume the frequency of all loads and stores is 36%
      How much faster a processor would run with a perfect cache that never missed?

## Slide 32
To measure and analyze cache performance (Cont.)
  Example: calculating cache performance (Cont.)
    Solution
      Assume there are total I instructions
      Instruction miss cycles = I  2%  100 = 2  I
      Data miss cycles = I  36%  4%  100 = 1.44  I
      Total number of memory-stall cycles: (2 + 1.44)  I = 3.44  I
      CPI with memory stalls: 2 + 3.44 = 5.44
      The ratio of the CPU execution times is:
  If the processor is made faster but the memory system is not
    The amount of time spent on memory stalls will take up an increasing fraction of the execution time
    In previous example, suppose the CPI is reduced from 2 to 1
      CPI of the system with cache miss: 1 + 3.44 = 4.44
      The system with the perfect cache will be 4.44 (4.44/1) times faster
      Execution time spent on memory stalls: 63% (CPI = 2) vs. 77% (CPI = 1)
    Increasing the clock rate without changing the memory system also increases the performance lost due to cache misses

## Slide 33
To measure and analyze cache performance (Cont.)
  A larger cache could have a longer access time (the increase in hit time)
    An increase in accessing a word from the memory system
    An increase in the processor cycle time
    Likely adds another stage to the pipeline
      It may take multiple cycles for a cache hit
    The increase in hit time for a larger cache could dominate the improvement in hit rate, leading to a decrease in processor performance
  Average memory access time (AMAT)
    AMAT = Time for a hit + Miss rate  Miss penalty
    The average time to access memory considering both hits and misses and the frequency of different accesses
    Example:
      Problem
        A processor with a 1 ns clock cycle time
        Miss penalty: 20 clock cycles Miss rate: 0.05 misses per instruction
        A cache access time (including hit detection): 1 clock cycle
        Find the AMAT for this processor
      Solution
        AMAT = Time for a hit + Miss rate  Miss penalty = 1 + 0.05  20 = 2 clock cycles = 2 ns

## Slide 34
Reducing cache misses by more flexible placement of blocks
  Different placement schemes
    Direct mapped
      A block can go in exactly one place in the cache
      Position: (Block number) modulo (Number of cache blocks)
    Fully associative
      A block can be placed in any location in the cache
      All tags of all the blocks in the cache must be searched (in parallel)
      Comparators significantly increase the hardware cost
      Only practical for caches with small numbers of blocks
    Set associative
      Each block can be placed in a fixed number of locations
      n-way set-associative cache
        A cache with n locations for a block
        A cache consists of a number of sets, each of which consists of n blocks
        Each block in the memory maps to a unique set in the cache given by the index field, and a block can be placed in any element of that set
        All tags of all the elements of the set must be searched
      Position: (Block number) modulo (Number of sets in the cache)

## Slide 35
Fig. 5.14 The location of a memory block whose address is 12 in a cache with 8 blocks varies for direct-mapped, set-associative, and fully associative placement.

## Slide 36
Reducing cache misses by more flexible placement of blocks (Cont.)
  To increase the degree of associativity
    A direct-mapped cache is simply a one-way set-associative cache
    A fully associative cache with m entries
      An m-way set-associative cache, only one set with m blocks
    Advantage: decreases the miss rate
    Disadvantage: increases in the hit time
Fig. 5.15 An eight-block cache configured as direct mapped, two-way set associative, four-way set associative, and fully associative.

## Slide 37
Reducing cache misses by more flexible placement of blocks (Cont.)
  Example: misses and associativity in caches
    Problem
      Three small cache, each consists of four one-word blocks
      Direct mapped, two-way set associative, fully associative
      Given a sequence of block addresses: 0, 8, 0, 6, 8
      Find the number of misses for each cache organization
    Solution
      Direct-mapped: 5 misses
      Two-way set associative: 4 misses
        Using the least recently used (LRU) replacement rule

## Slide 38
Reducing cache misses by more flexible placement of blocks (Cont.)
  Example: misses and associativity in caches (Cont.)
    Solution (Cont.)
      Fully-associative: 3 misses
        The best we can do
  Reduction in the miss rate vs. associativity
    64 KB data cache, 16-word block
    One-way to two-way associativity: 15% decreasing
    Little further improvement in going to higher associativity
Fig. 5.16 The data cache miss rates for an organization like the Intrinsity FastMATH processor for SPEC2000 benchmarks with associativity varying from one-way to eight-way.

## Slide 39
Locating a block in the cache
  Address decomposition
    Index: used to select the set containing the address of interest (n bits)
    Tag: all the tags in the selected set are searched in parallel
    Block offset: block offset (m bit) + byte offset (2 bits)
  Costs of an associative cache
    Extra comparators and n-to-1 multiplier
    Any delay imposed by having to do the compare and select from among the elements of the set
Fig. 5.18 The implementation of a four-way set-associative cache requires four comparators and a 4-to-1 multiplexor.
Fig. 5.17 The three portions of an address in a set-associative or direct-mapped cache.

## Slide 40
Locating a block in the cache (Cont.)
  The choice among three placement schemes
    Depending on the cost of a miss versus the cost of implementing associativity
    Both in time and in extra hardware
  Example: size of tags versus set associativity
    Problem
      A cache of 4096 blocks, 4-word block size, 32-bit address
      Find the total number of sets and the total number of tag bits for caches that are direct mapped, two-way set associative, four-way set associative, and full associative
    Solutions
      32-bit address: 4 bits for block offset, 28 bits for index and tag
      Direct mapped
        4096 sets Index: log2(4096) = 12 bits Tag: (28 – 12)  4096  66 K bits
      Two-way set associative
        2048 sets Index: log2(2048) = 11 bits Tag: (28 – 11)  2  2048  70 K bits
      Four-way set associative
        1024 sets Index: log2(1024) = 10 bits Tag: (28 – 10)  4  1024  74 K bits
      Fully associative
        1 sets Index: log2(1) = 0 bits Tag: (28 – 0)  4096  1  115 K bits

## Slide 41
Choosing which block to replace
  To choose a block among the blocks in the selected set to replace
  Least recently used (LRU)
    The block replaced is the one that has been unused for the longest time
    Implemented by keeping track of when each element in a set was used relative to the other elements in the set
    As associativity increases, implementing LRU gets harder
Reducing the miss penalty using multilevel caches
  Multilevel cache
    A memory hierarchy with multiple levels of caches
    To close the gap further between the fast clock rates of modern processors and the increasingly long time required to access DRAMs
  Using a second-level cache
    Normally on the same chip as the processor and primary cache
    To be accessed when a miss occurs in the primary cache
      The access time is much less than the access time of main memory
    If neither the primary nor secondary cache contains the data, a main memory access is required and incurred a larger miss penalty

## Slide 42
Reducing the miss penalty using multilevel caches (Cont.)
  Example: performance of multilevel caches
    Problem
      A processor with a base CPI of 1.0 and a clock rate of 4 GHz
      Main memory access time: 100 ns Secondary cache access time: 5 ns
      Miss rate per instruction at the primary cache: 2%
      After adding a secondary cache, the miss rate to main memory is 0.5%
      How much faster will the processor with and without a secondary cache?
    Solution 1
      Miss penalty to main memory: 100 ns  400 clock cycles
      Miss penalty to secondary cache: 5 ns  20 clock cycles
      For the processor with one level of caching
        Total CPI = Base CPI + Memory-stall cycles per instruction
        Total CPI = 1.0 + 2%  400 = 9
      For the processor with two level of caching
        Total CPI = Base CPI + Primary stalls per instruction + Secondary stalls per instruction
        Total CPI = 1 + 2%  20 + 0.5%  400 = 3.4
      Relative performance: 9/3.4 = 2.6
    Solution 2
      For the processor with two level of caching
        Total CPI = 1 + (2% – 0.5%)  20 + 0.5%  (20 + 400) = 3.4

## Slide 43
Reducing the miss penalty using multilevel caches (Cont.)
  Design considerations for a primary and secondary cache
    Primary cache
      To focus on minimizing hit time to yield a shorter clock cycle or fewer pipeline stages
      Smaller cache size, higher miss rate
      Smaller block size to reduce the miss penalty
    Secondary cache
      To focus on miss rate to reduce the penalty of long memory access times
      Larger cache size, the access time is less critical
      Larger block size
      Higher associativity to reduce miss rates
Elaboration
  Global miss rate
    The fraction of references that miss in all levels of a multilevel cache
  Local miss rate
    The fraction of references to one level of a cache that miss; used in multilevel hierarchies

## Slide 44: Dependable Memory Hierarchy
Defining failure
  Dependability
    A system alternating between two states
      Service accomplishment, where the service is delivered as specified
      Service interruption, where the delivered service is different from the specified service
    Failure: service accomplishment  service interruption
    Restoration: service interruption  service accomplishment
    Failures can be permanent or intermittent
      Intermittent failures are harder to diagnose the problem when a system oscillates between above two states
      Permanent failures are far easier to diagnose
  Reliability
    Mean time to failure (MTTF)
      A measure of the continuous service accomplishment from a reference point
      When MTTF gets large it can be misleading

## Slide 45
Defining failure (Cont.)
  Reliability (Cont.)
    Annual failure rate (AFR)
      The percentage of devices that would be expected to fail in a year for a given MTTF
      AFR leads to better intuition
    Example: MTTF vs. AFR
      Problem
        Disks are quoted to have a 1,000,000-hour MTTF ( 114 years)
        50,000 servers, each server has 2 disks
        Use AFR to calculate how many disks we would expect to fail per year
      Solution
        One year is 365  24 = 8760 hours
        1,000,000-hour MTTF  AFR = 8760/1,000,000 = 0.876%
        With 100,000 disks, we expect 876 disks to fail per year (2 disk failures per day)
    Mean time to repair (MTTR): the time of service interruption
    Mean time between failures (MTBF): MTBF = MTTF + MTTR
  Availability
    A measure of service accomplishment with respect to the alternation between the two states of accomplishment and interruption
    Availability = MTTF / (MTTF + MTTR)

## Slide 46
Defining failure (Cont.)
  Dependability vs. Reliability vs. Availability
    Dependability is just synonyms
    Reliability and availability are actually quantifiable measures
    Shrinking MTTR can help availability as much as increasing MTTF
      Tools for fault detection, diagnosis, and repair help reduce the time to repair faults
  The number of nines of availability per year
    Definition
      One nine: 90%  36.5 days of repair/year
      Two nines: 99%  3.65 days of repair/year
      Three nines: 99.9%  526 minutes of repair/year
      Four nines: 99.99%  52.6 minutes of repair/year
      Five nines: 99.999%  5.26 minutes of repair/year
    Example:
      A very good Internet service today offers 4 or 5 nines of availability
  Failure vs. Fault
    Failure needs to be defined with respect to a context
    Failure of a component may not lead to a failure of the system
    Fault: failure of a component

## Slide 47
Defining failure (Cont.)
  Three ways to improve MTTF
    Fault avoidance
      Preventing fault occurrence by construction
    Fault tolerance
      Using redundancy to allow the service to comply with the service specification despite faults occurring
    Fault forecasting
      Predicting the presence and creation of faults, allowing the component to be replaced before it fails
The Hamming Single Error Correcting, Double Error Detecting Code (SEC/DED)
  Self-study

## Slide 48: Virtual Memory
Preliminary
  Virtual memory
    A technique that uses main memory as a cache for secondary storage
  Two major motivations for virtual memory
    To allow efficient and safe sharing of memory among multiple programs
      Such as for the memory needed by multiple virtual machines for cloud computing
    To remove the programming burdens of a small, limited amount of main memory
  The first motivation
    Consider multiple virtual machines running at once on a computer
      The total required memory size may be much larger than the available size
      Main memory need contain only the active portions of the many virtual machines
        Only a fraction of total required memory is actively being used at any point in time
      Must be able to protect the virtual machines from each other
        To ensure that a program can only access the portions of main memory that have been assigned to it

## Slide 49
Preliminary (Cont.)
  The first motivation (Cont.)
    The virtual machines sharing the memory change dynamically while the virtual machines are running
      To compile each program into its own address space
      Virtual memory implements the translation of a program’s address space to physical addresses
      The translation process enforces protection of a program’s address space from other virtual machine
  The second motivation
    If a program became too large for memory, it was up to the programmer to make it fit
      Programmers divided programs into mutually exclusive pieces
      Overlays were loaded or unloaded under user program control during execution
      The program never tried to access an unloaded overlay
      The overlays loaded never exceeded the total size of the memory
      Overlays were traditionally organized as modules, each containing both code and data
    Virtual memory automatically manages the main memory (physical memory) and secondary storage

## Slide 50
The structure of virtual memory
  Terminologies in virtual memory system
    Page: a virtual memory block
    Page fault: a virtual memory miss
    Virtual address
      An address that corresponds to a location in virtual space
      To be translated by address mapping to a physical address when memory is accessed
    Address translation (address mapping)
      The process by which a virtual address is mapped to an address used to access memory
Fig. 5.25 In virtual memory, blocks of memory are mapped from one set of addresses to another set.

## Slide 51
The structure of virtual memory (Cont.)
  Relocation
    To map the virtual addresses to different physical addresses before the addresses are used to access memory
      Program can be loaded to anywhere in main memory
    All virtual memory systems relocate the program as a set of pages
      To eliminate the need to find a contiguous block of memory to allocate a program
      The operating system only need to find a sufficient number of pages in main memory
  Virtual address format
    Page offset
      Not changed during address translation
      To determine the page size
    Virtual page number
      To be translate to physical page number during
      address translation
    The number of pages addressable with the virtual
    addresses need not match those of addressable
    with the physical addresses
      The number of virtual pages is larger
Fig. 5.26 Mapping from a virtual to a physical address.

## Slide 52
The structure of virtual memory (Cont.)
  A page fault will take millions of clock cycles to process
    Dominated by the time to get the first word for typical page sizes
  Key decisions in designing virtual memory systems
    Pages should be large enough to amortize the high access time
      Typical size: 4 KB ~ 16 KB
      New desktop and server system: to support 32 KB and 64 KB
      New embedded system: 1 KB
    Organizations that reduce the page fault rate are attractive
      To allow fully associative placement
    Page faults can be handled in software
      The overhead will be small compared to the disk access time
      To use clever algorithms for choosing how to place pages
    Write-through will not work for virtual memory
      Writes take too long
      Virtual memory system uses write-back

## Slide 53
Placing a page and finding it again
  Using fully associative placement of pages
    To reduce page fault frequency
    To use a clever and flexible replacement scheme
      To use a sophisticated algorithm and complex data structure to track page usage
      To try to choose a page that will not be needed for a long time
  Page table
    The table containing the virtual to physical address translations
      Resided in memory, to avoid a full search of memory
      Indexed with the page number from the virtual address to discover the corresponding physical page number
    Each program has its own page table
      Different programs use the same virtual addresses
    The page table may contain entries for pages not present in memory
      A valid bit is used in each page table entry
    No tags are required
      The page table contains a mapping for every possible virtual page
    Page table register
      A register that points to the start of the page table

## Slide 54
Fig. 5.27 The page table is indexed with the virtual page number to obtain the corresponding portion of the physical address.

## Slide 55
Page faults
  A page fault occurs if the valid bit for a virtual page is off
    The operating system gets control, done with the exception mechanism
    To find the page in the next level of the hierarchy and decide where to place the requested page
  When a process is created, the operating system creates
    A swap space on flash memory or disk
      The space reserved for the full virtual memory space of a process
    A data structure to record where each virtual page is stored on disk
      Part of the page table
      An auxiliary data structure indexed in the same way as the page table
Fig. 5.28 The page table maps each page in virtual memory to either a page in main memory or a page stored on disk, which is the next level in the hierarchy.

## Slide 56
Page faults (Cont.)
  The operating system tracks which processes and which virtual addresses use each physical page
    When a page fault occurs and all pages in memory are in use
      Usually follow the least recently used (LRU) replacement scheme
      The replaced pages are written to swap space on the disk
    Approximate LRU replacement scheme
      To keep track which pages have and which pages have not been recently used
      Use bit (reference bit)
        To be set whenever a page is accessed
        The operating system periodically clears the reference bits
        To determine which pages were touched during a particular time period
      The operating system will replace a page which reference bit is off
What about writes?
  Virtual memory must use write-back scheme
  Dirty bit
    A dirty bit is associated with each page in the page table
    To be set if any word in a page is written
      To indicate whether the page needs to be written out when it is replaced

## Slide 57
Making address translation fast: the TLB
  Every memory access by a program can take at least twice as long
    One memory access to the page table to obtain the physical address
    A second access to get the data
  Translation lookaside buffer (TLB)
    A special cache that keeps track of recently used translations
    Tag entry: virtual page number Data entry: physical page number
    Valid bit, dirty bit, reference bit
Fig. 5.29 The TLB acts as a cache on the page table for the entries that map to physical pages only.

## Slide 58
Making address translation fast: the TLB (Cont.)
  On every reference, we access the TLB instead of the page table
    To look up the virtual page number in the TLB
    TLB hit
      The physical page number is used to form the address
      The corresponding reference bit is turned on
      The dirty bit is turned on if the processor is performing a write
    TLB miss
      Merely TLB miss
        The page exists in memory, only the translation is missing in the TLB
        To load the translation from the page table and replace an TLB entry
        To copy the reference and dirty bits back to the page table entry when a TLB entry is replaced (write-back scheme)
      True page fault
        The page is not present in memory
        To invoke the operating system using an exception
      Merely TLB miss will be much more frequent than true page faults
    The TLB miss rate is expected to very small
    TLB misses can be handled either in hardware or in software
      With care there can be little performance between the two approaches

## Slide 59
Making address translation fast: the TLB (Cont.)
  Typical values for a TLB
    TLB size: 16 ~ 512 entries
    Block size: 1 ~ 2 page table entries (typically 4~8 bytes each)
    Hit time: 0.5 ~ 1 clock cycle
    Miss penalty: 10 ~ 100 clock cycles Miss rate: 0.01% ~ 1%
  Associativities in TLBs
    Small and fully associative TLBs
      Lower miss rate
      Since the TLB is small, the cost of a fully associativity mapping is not too high
      Choosing the entry to replaced becomes tricky since implementing a hardware LRU scheme is too expensive
      Randomly choosing an entry to replace
    Larger TLBs with small associativity
  Example: the Intrinsity FastMATH TLB
    4 KB pages, 32-bit address space  The virtual page number is 20 bits long
    The physical address is the same size as the virtual address
    The TLB contains 16 entries, fully associative
    Each TLB entry is 64 bits wide (bookkeeping bits)

## Slide 60
Fig. 5.30 The TLB and cache implement the process of going from a virtual address to a data item in the Intrinsity FastMATH.

## Slide 61
Fig. 5.31 Processing a read or a write through in the Intrinsity FastMATH TLB and cache.

## Slide 62
Integrating virtual memory, TLBs, and caches
  Data cannot be in the cache unless it is present in main memory
  The operating system helps maintain the memory hierarchy
    To flush the contents of any page from the cache when it decides to migrate that page to disk
    To modify the page tables and TLB
    To generate a page fault when the processor tries to access any data on the migrated page
  Example: overall operation of a memory hierarchy
    In a memory hierarchy includes a TLB and a cache
    Three different types of misses: TLB miss, page fault, cache miss
    Consider all the combinations of these three events with one or more occurring
    State whether this event can actually occur and under what circumstances
Fig. 5.32 The possible combinations of events in the TLB, virtual memory system, and cache.

## Slide 63
Implementing protection with virtual memory
  To allow sharing of a single main memory by multiple processes and provide memory protection among these processes and the operating system
    To ensure one renegade process cannot write into the address space of another user process or into the operating system
    The write access bit in the TLB can protect a page from being write
  Basic capabilities must be provided by the operating system
    At least two modes
      User mode: the running process is a user process
      Kernel (supervisor) mode: the running process is an operating system process
    A portion of the processor state that a user process can read but not write
      Including the user/supervisor mode bit, the page table pointer, and the TLB
      The operating system uses special instructions that are only available in supervisor mode to write these element
    Alternating between user and supervisor modes
      User mode  supervisor mode
        Using a special system call instruction
        The PC from the point of the system call is saved in the EPC
      Supervisor mode  user mode
        Using the return from exception (ERET) instruction

## Slide 64
Implementing protection with virtual memory (Cont.)
  To prevent a process from reading the data of another process
    Each process has it own virtual address space
    The operating system keeps the page tables organized and let the independent virtual pages map to disjoint physical pages
      One process will not be able to access another’s data
    To place the page tables in the protected address space
      The operating system can assure safety if it prevents the user process from modifying its own page table
      The operating system must be able to modify the page tables
  When processes want to share information in a limited way
    The operating system must assist them
      It requires changing the page table
    The write access bit can be used to restrict the sharing to just read sharing
    To allow process P1 to read a page owned by process P2
      P2 would ask the operating system to let a virtual page in P1’s address space point to the same physical page that P2 wants to share
      The write protection bit can be used to prevent P1 from writing the data
      Any bits that determine the access rights must be included in both the page table and the TLB

## Slide 65
Handling TLB misses and page faults
  Two possibilities of TLB miss
    Merely TLB miss
      The page is present in memory
      Only need to create the missing TLB entry
    Page fault
      The page is not present in memory
      Need to transfer control to the operating system
  MIPS traditionally handles a TLB miss in software
    To bring in the page table entry from memory and re-execute the instruction
    To generate a page fault exception if necessary
  Using the exception mechanism to handle a TLB miss
    To interrupt the active process  to transfer control to the OS  to resume execution of the interrupted process
      PC of the instruction caused the TLB miss must be saved in the EPC
    The exception must be asserted by the end of the same clock cycle that the memory access occurs
      A page fault will be recognized during the clock cycle used to access memory
      The next clock cycle will begin exception processing

## Slide 66
Handling TLB misses and page faults (Cont.)
  Once the operating system knows the virtual address that caused the page fault (for instruction access)
    Find the location of the referenced page on disk
      Using the virtual address to look up the page table entry
    Choose a physical page to replace
      If the chosen page is dirty, it must be written out to disk
    Start a read to bring the referenced page from disk into the chosen physical page
      It may take millions of processor clock cycle
      The operating system will usually select another process to execute until the disk access completes
    Re-execute the instruction that faulted
      Restore the PC and state of the process that caused the page fault
      Reset the processor from kernel to user mode
      Access the requested page successfully and continue execution
  Page fault exceptions for data accesses are difficult to implement
    They occur in the middle of instructions
    The instruction cannot be completed before handling the exception
    The instruction must be restarted after handling the exception

## Slide 67
Handling TLB misses and page faults (Cont.)
  Making instructions restartable
    The exception can be handled and the instruction later continued
    For an architecture like the MIPS: easy
      Each instruction writes only one data item and this write occurs at the end of the instruction cycle
      Simply prevents the instruction from completing and restarts the instruction at the beginning
    For processors with complex instructions: hard
      Each instruction my touch many memory locations and write many data items
       To generate a number of page faults
      Instruction often cannot be restarted from the beginning
       To interrupt and later continue midstream in its execution
      To resume an instruction in the middle of its execution, it requires saving some special state during the execution
      Careful and detailed coordination between the exception-handling code in the operating system and the hardware
  Example: how MIPS architecture works when a TLB miss occurs

## Slide 68
Handling TLB misses and page faults (Cont.)
  If page faults occur too frequently
    A program routinely accesses more virtual memory than it has physical memory
    Thrashing
      A program continuously swaps pages between memory and disk
      The program will run very slowly
    Solutions
      Using a computer with more memory
      To reexamine the algorithm and data structure to change the locality
Fig. 5.35 The key quantitative design parameters that characterize the major elements of memory hierarchy in a computer.

## Slide 69: A Common Framework for Memory Hierarchies
Question 1: Where can a block be placed?
  Direct mapped, set associative, fully associative
  The advantage of higher degree of associativity: the lower miss rate
    Reducing misses that compete for the same location
    The largest gains are obtained in going from one-way to two-way associative
    As cache sizes grow, the relative improvement increases only slightly
  The potential disadvantages of associativity
    Increased cost, slower access time
Fig. 5.30 The data cache miss rates for each of eight cache sizes improve as the associativity increases.

## Slide 70
Question 2: How is a block found?
  The choice among three block placement schemes
    Depending on the cost of a miss versus the cost of implementing associativity
      Both in time and in extra hardware
    Including the L2 cache on the chip enables much higher associativity
      The hit times are not as critical
    Fully associative caches are prohibitive except for small sizes
      The cost of the comparators is not overwhelming
      The absolute miss rate improvements are greatest
  Four location methods
    Indexing: used in direct-mapped cache
      A few systems have used it because of their advantages in access time and simplicity
      Finding the requested block does not depend on a comparison
    Fully search: used in fully-associative cache

## Slide 71
Question 2: How is a block found? (Cont.)
  Four location methods (Cont.)
    Limited search: used in set-associative cache
      Often used for caches and TLB
      The access combines indexing and the search of a small set
    A separate lookup table
      Example: page table for the virtual memory system
      Extra storage and extra memory access is required
      The motivation for choosing fully-associative placement and the extra table
        Fully associativity is beneficial since misses are very expensive
        Fully associativity allows the software to use sophisticated replacement schemes that are designed to reduce the miss rate
        The full map can be easily indexed with no extra hardware and no searching required
        The large page size means the page table size is relatively small
Question 3: Which block should be replaced on a cache miss?
  Number of candidates
    In a fully associativity cache, all blocks are candidates for replacement
    In a set-associative cache, candidates are chosen among the blocks in the set
    In a direct-mapped cache, there is only one candidate

## Slide 72
Question 3: Which block should be replaced on a cache miss? (Cont.)
  Primary replacement strategies in set-associative or fully associative caches
    Random
      Candidate blocks are randomly selected
      Simple to build in hardware
    Least recently used (LRU)
      To replace the block that has been unused for the longest time
      Too costly to implement for caches with more than a small degree of associativity
      Approximated LRU
        Used for four-way or larger set-associativity cache
        Tracking which set is LRU, and which block in each set is LRU
    Random replacement can sometimes be better than the simple LRU approximations
  For larger associativity, either approximated LRU or random replacement can be used
  As the cache become larger
    The miss rate for both replacement strategies falls
    The absolute difference becomes small

## Slide 73
Question 3: Which block should be replaced on a cache miss? (Cont.)
  In virtual memory
    A tiny reduction in the miss rate can be important
    Approximated LRU implemented in software is acceptable
      Misses are so expensive and relatively infrequent
Question 4: What happens on a write?
  Write-through vs. Write-back
    Only write-back policy is practical in virtual memory systems
    Today lowest-level caches typically use write-back
  Advantages of both policies
    Write-through
      Misses are simpler and cheaper
      Easier to implement although a write buffer is required
    Write-back
      Individual words can be written at the rate that the cache can accept them
      Multiple writes within a block require only one write to the lower level in the hierarchy
      To make effective use of a high-bandwidth transfer since the entire block is written

## Slide 74
The three Cs: An intuitive model for understanding the behavior of memory hierarchies
  Three Cs model
    A qualitative cache model in which all cache misses are classified into one of three categories
    Compulsory misses (cold-start misses)
      Caused by the first access to a block that has never been in the cache
    Capacity misses
      Caused when the cache cannot contain all the blocks needed during execution
      To occur when blocks are replaced and then later retrieved
    Conflict misses (collision misses)
      Occur in set-associative or direct-mapped caches when multiple blocks compete for the same set
      Can be eliminated in a fully associative
      cache of the same size
Fig. 5.37 The miss rate can be broken into three sources of misses.

## Slide 75
The three Cs: An intuitive model for understanding the behavior of memory hierarchies (Cont.)
  Methods to attack three categories of misses
    Conflict misses
      To increase associativity
      May slow access time to lower overall performance
    Capacity misses
      To enlarge the cache
      The increased access time could lead to lower overall performance
      Second-level caches have been growing steadily larger for many years
      First-level caches have been growing slowly, if at al
    Compulsory misses
      To increase the block size
      Too large block will lead too high miss penalty
Fig. 5.32 Memory hierarchy design challenges.

## Slide 76: Using a Finite-State Machine to Control a Simple Cache
A simple cache
  Key characteristics of the cache
    Direct-mapped
    Write-back using write allocate
    Block size: 4 words (16 bytes, 128 bits) Cache size: 16 KB (1024 blocks)
    The cache includes a valid bit and dirty bit per block
  Cache address
    32-bit byte address
  Signals between the processor, cache, and memory
CPU
Cache
Memory
Read/Write
32
32
32
32
128
128
Read/Write
Valid
Valid
Address
Address
Data
Data
Data
Data
Ready
Ready
Tag | Cache index | Block offset
18 bits | 10 bits | 4 bits

## Slide 77
Finite-state machines
  A sequential logic consists of
    A set of states, inputs, and outputs
    Next-state function
      To map the current state and the inputs to a new state
    Output function
      To map the current state and possibly the inputs to a set of asserted outputs
  The implementation
    A temporary register holds the current state
    A block of combinational logic determines both the datapath signals to be asserted and the next state
Fig. 5.39 Finite-state machine controllers are typically implemented using a block of combinational logic and a register to hold the current state.

## Slide 78
FSM for a simple cache controller
Fig. 5.40 Four states of the simple controller.

## Slide 79: Real Stuff: The ARM Cortex-A8 and Intel Core i7 Memory Hierarchies
Fig. 5.43 Address translation and TLB hardware for the ARM Cortex-A8 and Intel Core i7 920.

## Slide 80
Fig. 5.44 Caches in the ARM Cortex-A8 and Intel Core i7 920.

## Slide 81
Fig. 5.45 Data cache miss rates for ARM Cortex-A8 when running Minnespec, a small version of SPEC2000.
Fig. 5.47 The L1, L2, and L3 data cache miss rates for the Intel Core i7 920 running the full integer SPECCPU2006 benchmarks.

## Slide 82
Fig. 5.46 The average memory access penalty in clock cycles per data memory reference coming from L1 and L2 is shown for the ARM processor when running Minnespec.

## Slide 83: Fallacies and Pitfalls
Pitfalls
  Forgetting to account for byte addressing or the cache block size in simulating a cache
    To make sure to account for the effect of byte addressing and multiword blocks
    Example: 32-byte direct-mapped cache, block size is 4 bytes
      The byte address 36 maps into block 1
        Byte address 36 is block address 9 and (9 mod 8) = 1
      The word address 36 maps into block 4
        (36 mod 8) = 4
    Example: 256-byte direct-mapped cache, block size is 32 bytes
      The byte address 300 maps into block 1
        The number of blocks in the cache is (256/32) = 8
        Byte address 300 is block address 9 and (9 mod 8) = 1

## Slide 84
Pitfalls (Cont.)
  Ignoring memory system behavior when writing programs or when generating code in a compiler
    Equivalent fallacy
      Programmers can ignore memory hierarchies in writing code
    Example: matrix multiply, 500  500 double precision matrices
      for (i = 0; i != 500; i = i + 1)
      for (j = 0; j != 500; j = j + 1)
      for (k = 0; k != 500; k = k + 1)
      x [i][j] = x [i][j] + y [i][k]  z [k][j]
      Using a MIPS CPU with a 1 MB 2nd cache, loop order k  j  i costs about half the execution time
  Having less set associativity for a shared cache than the number of cores or threads sharing that cache
    A parallel program running on 2n processors or threads can easily allocate data structures to addresses that would map to the same set of a shared L2 cache
    If the L2 cache is less than 2n-way associative, it will occur performance bugs due to conflict misses in L2 cache

## Slide 85
Pitfalls (Cont.)
  Using average memory access time to evaluate the memory hierarchy of an out-of-order processor
    When a processor stalls during a cache miss
      Separately calculate the memory-stall time and the processor execution time
      To evaluate the memory hierarchy independently using average memory access time
    For an out-of-order processor
      The processor continues to execute instructions and may even sustain more cache misses during a cache miss
      The out-of-order processor must be simulated along with the memory hierarchy
Fallacies
  Disk failure rates in the field match their specifications
    Study 1
      Almost 100,000 disks
      Quoted MTTF 1,000,000 ~ 1,500,000 AFR 0.6% ~ 0.8%
      In the field: 2% ~ 4%
    Study 2
      100,000 disks at Google with quoted AFR 1.5%
      In the field: 1.7% in the 1st year, 8.6% in the 3rd year

## Slide 86
Fallacies (Cont.)
  Operating systems are the best place to schedule disk accesses
    Higher-level disk interfaces offer logical block addresses to the hose operating system
      An operating system can try to sort the logical block addresses into increasing order to help performance
    The disk can reduce the rotational and seed latencies by rescheduling the logical block addresses
      Only the disk knows the actual mapping of the logical addresses onto the physical geometry of sectors, tracks, and surfaces
    Example
The sequence after reordering by OS
The original read sequence
Fig. 5.50 Example showing OS vs. disk schedule accesses, labeled host-ordered vs. drive-ordered.