## Slide 1: The Processor

## Slide 2: Outline
Introduction
Logic Design Conventions
Building a Datapath
A Simple Implementation Scheme
An Overview of Pipelining
Pipelined Datapath and Control
Data Hazards: Forwarding versus Stalling
Control Hazards
Exceptions
Parallelism via Instructions
Real Stuff: The ARM Cortex-A8 and Intel Core i7 Pipelines
Fallacies and Pitfalls

## Slide 3: Introduction
Preliminary
  The performance of a machine was determined by three key factors
    Instruction count, clock cycle time, CPI
    Both the clock cycle time and the CPI are determined by the implementation of the processor
  In this chapter
    To construct the datapath and control unit of the MIPS instruction set
      A highly abstract and simplified overview
      To build up a datapath and construct a simple version of a processor
      A more realistic pipelined MIPS implementation
      To implement more complex instruction sets (x86)
    Make the common case fast
    Simplicity favors regularity

## Slide 4
A basic MIPS implementation (Cont.)
  An implementation includes the following instruction
    Memory-reference instructions lw, sw
    Arithmetic-logical instructions add, sub, and, or, slt
    Branch instructions beq, j
  An overview of the implementation
    Execution steps
      Step 1: send the program counter (PC) to the memory to fetch the instruction
      Step 2: read one or two registers
        Using fields of the instruction to select the registers to read
        lw: read one register
        Other instructions: read two registers
      Step 3: use arithmetic-logical unit (ALU)
        lw, sw: address calculation
        add, sub, and, or, slt: operation execution
        beq: comparison
        j: doesn’t use ALU
      Step 4 & 5: actions depend on different instruction types
        lw, sw: access the memory
        add, sub, and, or, slt: write the register file
        beq, j: change the PC, otherwise the PC should be incremented by 4

## Slide 5
A basic MIPS implementation (Cont.)
  An overview of the implementation (Cont.)
    The abstract view of a MIPS implementation
      Multiplexors, which select from among several inputs based on the setting of its control lines, are omitted
      The control unit and control lines are omitted
Fig. 4.1 An abstract view of the implementation of the MIPS subset showing the major functional units and the major connections between them.

## Slide 6
A basic MIPS implementation (Cont.)
  An overview of the implementation (Cont.)
    The datapath of the MIPS implementation
      Three required multiplexors are added
      A control unit and control lines for the major functional units are added
Fig. 4.2 The basic implementation of the MIPS subset, including the necessary multiplexors and control lines.

## Slide 7: Logic Design Conventions
The datapath elements in the MIPS implementation
  Logic element that operates on data values
    Combinational logic (no internal storage)
      The outputs depend only on the current inputs
    Given the same input always produces the same output
    Ex: ALU
  Logic element that contains state (state element)
    Sequential logic (internal storage)
      The outputs depend on both inputs and contents of the internal state
    At least two inputs and one output
      Input: data value
      Input: clock
        Used to determine when the state element should be written
        The state element can be read at any time
      Output: the value written in an earlier clock cycle
    Ex: instruction/data memory, register

## Slide 8
Clocking methodology
  To define when signals can be read and written
    If a signal is written and read at the same time, the value of the read will be unpredictable!
  Edge-triggered
    Any values stored in a state element are updated only on a clock edge
    For a combinational logic
      Inputs and outputs must be state elements
      Inputs: values written in a previous clock cycle
      Outputs: values can be used in a following clock cycle
      All signals must propagate through the combinational logic in the time of one clock cycle
      The time necessary for the signals to reach outputs defines the length of the clock cycle
Fig. 4.3 Combinational logic, state elements, and the clock are closely related.

## Slide 9
Clocking methodology (Cont.)
  Edge-triggered (Cont.)
    Control signal vs. Data signal
      Control signal
        Used for multiplexor selection or for directing the operation of a functional unit
        The state element is changed only when the write control signal is asserted and a clock edge occurs
        If a state element is written on every active clock edge, the control signal is often omitted
        If a state element is not updated on every clock, then an explicit write control signal is required
      Data signal
        To contain information that is operated on by a functional unit
    Terminologies
      Asserted/deasserted: a signal is logically high/low
      Assert/deassert: a signal should be driven logically high/low
    To allow a state element to be read and written in the same clock cycle
      The following steps are done in the same clock cycle
        To read the contents of a register
        To send the value through some combinational logic
        To write the same register
      No feedback within a single clock cycle

## Slide 10: Building a Datapath
The datapath elements in the MIPS implementation
  Elements used to fetch instructions and increment the PC
    Instruction memory
      A memory unit to store instruction of a program and supply instructions given an address
    Program counter (PC)
      A register holds the address of the current instruction
    Adder
      To increment the PC by 4 to the address of the next instruction
      An ALU that the control always specifies an add operation
Fig. 4.5 Two state elements are needed to store and access instructions, and an adder is needed to compute the next instruction address.
Fig. 4.6 A portion of the datapath used for fetching instructions and incrementing the program counter.

## Slide 11
The datapath elements in the MIPS implementation (Cont.)
  Register file
    A collection of 32 32-bit general-purpose registers
    Any register can be read or written by specifying its register number
    Four inputs and two outputs in total
      To read a data word
        An input to specify the register number to be read (5 bits)
        An output to carry the value been read
        The register file always outputs the contents of whatever register numbers are on the Read register inputs
      To write a data word
        An input to specify the register number to be written
        An input to supply the data to be written into the register
        To occur at the clock edge and the write control signal is asserted
Fig. 4.7 The two elements needed to implement R-format ALU operations are the register file and the ALU.

## Slide 12
The datapath elements in the MIPS implementation (Cont.)
  Arithmetic logic unit (ALU)
    To take two 32-bit inputs and produce a 32-bit result
    A 1-bit Zero signal to indicate the result is 0
    4-bit control signals
  Data memory
    A state element to store data
    Two inputs for the address and the write data
    A single output for the read result
    Separate read and write controls
      To read the value of an invalid address can cause problems
  Sign extension unit: 16 bits  32 bits
    To replicate the high-order sign bit of the original data item
Fig. 4.8 The two units needed to implement loads and stores, in addition to the register file and ALU, are the data memory unit and the sign extension unit.

## Slide 13
For different classes of instruction
  add/sub/and/or/sll $t1, $t2, $t3
    Fetching instructions and incrementing the PC
    Register file: to read operands in $t2 and $t3, to write result to $t1
    ALU: to operate
  lw/sw $t1, offset($t2)
    Fetching instructions and incrementing the PC
    Register file: to read the base register $t2, to write/read data to/from $t1
    Sign extension: to sign-extend the 16-bit offset to a 32-bit signed value
    ALU: to compute a memory address (base register $t2 + offset)
    Data memory: to read/write data
  beq $t1, $t2, offset
    Fetching instructions and incrementing the PC
    Register file: to read registers $t1 and $t2 for comparison
    Sign extension: to sign-extend the 16-bit offset to a 32-bit signed value
    Adder: to compute the branch target address (PC + offset)
      Shifter: to left shift the (sign-extended) offset by 2

## Slide 14
For different classes of instruction (Cont.)
  beq $t1, $t2, offset (Cont.)
    ALU: to compare contents of registers $t1 and $t2 by subtraction
      Using the zero signal to indicate whether the operands are equal or not
      Branch taken: Zero = 1  new PC = branch target address
      Branch not taken: Zero = 0  new PC = PC
  j offset
    Fetching instructions and incrementing the PC
    Shifter: to left shift the offset by 2 (26 bits  28 bits)
    To replace the lower 28 bits of PC
Fig. 4.9 The datapath for a branch uses the ALU to evaluate the branch condition and a separate adder to compute the branch target as the sum of the incremented PC and the sign-extended, lower 16 bits of the instruction, shifted left 2 bits.

## Slide 15
Creating a single datapath
  To execute all instructions in one clock cycle
    No datapath resource can be used more than once per instruction
      Any element needed more than once must be duplicated
      Separate instruction and data memories
    Some elements can be shared by different instruction flows
      Using a multiplexor and control signal to select among the multiple inputs
  Example: building a datapath
    To build a datapath for memory references and R-type instructions using a single register file and a single ALU
    Using the ALU
      R-type instruction: inputs coming from two registers
      Memory reference: the 2nd input is the sign-extended 16-bit offset
       A multiplexor is needed for the 2nd ALU input
    The value stored into a destination register
      R-type instruction: from the ALU
      Memory reference: from the memory (for a load)
       A multiplexor is needed for the data stored into the register file

## Slide 16
Creating a single datapath (Cont.)
  Example: building a datapath (Cont.)
Fig. 4.10 The datapath for the memory instructions and the R-type instructions.

## Slide 17
Creating a single datapath (Cont.)
  To combine all the pieces to make a simple datapath
    A multiplexor is required to select either the PC + 4 or the branch target address to be written into the PC
    A control unit is added to take inputs and generate
      A write signal for each state element
      The selector control for each multiplexor
      The ALU control
Fig. 4.11 The simple datapath for the MIPS architecture combines the elements required by different instruction classes.

## Slide 18: A Simple Implementation Scheme
The ALU control
  The ALU has 4 control inputs but only 6 combinations are used
  A small ALU control unit to generate the 4-bit ALU control input
    Inputs: the funct field of the instruction and a 2-bit ALUOp
      ALUOp = 00: addition for lw/sw
      ALUOp = 01: subtraction for beq
      ALUOp = 10: for R-type instructions, determined by the operation encoded in the funct field
    Output: a 4-bit signal that directly controls the ALU
ALU control lines | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR

## Slide 19
The ALU control (Cont.)
  Multiple levels of decoding
    The main control unit generates the ALUOp bits
    ALUOp bits are used as input to the ALU control unit that generate the actual signals to control the ALU unit
    Can reduce the size of the main control unit
    Potentially increase the speed of the control unit
      The speed of the control unit is often critical to clock cycle time
  To implement the ALU control unit: truth table
Fig. 4.13 The truth table for the three ALU control bits (called Operation).

## Slide 20
Designing the main control unit
  Observations about instruction formats
    op field (opcode) in bits 31:26
      To denote the operation and format of an instruction (Op [5:0])
    rs and rt fields at positions 25:21 and 20:16
      To specify the two registers to be read, for R-type, beq, sw instructions
    The base register for lw and sw is in bits 25:21 (rs)
    The 16-bit offset for beq, lw, and sw is in positions 15:0
    Destination register
      For lw is in bits 20:16 (rt) For R-type is in bits 15:11 (rd)
       A multiplexor is needed to select which field of the instruction is used to indicate the register number to be written
Fig. 4.14 The three instruction classes (R-type, load and store, and branch use two different instruction formats.
R
R
R
R
W/R
R
W

## Slide 21
Designing the main control unit (Cont.)
  The datapath with multiplexors and control signals
    ALU control unit, 4 multiplexors, 7 single-bit control lines, and a 2-bit ALUOp control signal
      All the multiplexors have two inputs and require a single control line
Fig. 4.15 The datapath of Figure 4.11 with all necessary multiplexors and all control lines identified.

## Slide 22
Designing the main control unit (Cont.)
  The datapath with multiplexors and control signals (Cont.)
    The function of each of the control signals
      All but PCSrc can be set based solely on the opcode
      PCSrc should be asserted if the instruction is beq and the Zero output of the ALU is asserted (PCSrc = Branch AND Zero)
Fig. 4.16 The effect of each of the seven control signals.
Signal name | Effect when deasserted (0) | Effect when asserted (1)
RegDst | The register destination number for the Write register comes from the rt field (bits 20:16) | The register destination number for the Write register comes from the rd field (bits 15:11)
RegWrite | None | The register on the Write register input is written with the value on the Write data input
ALUSrc | The second ALU operand comes from the second register file output (Read data 2) | The second ALU operand is the sign-extended, lower 16 bits of the instruction
PCSrc | The PC is replaced by the output of the adder that computes the value of PC + 4 | The PC is replaced by the output of the adder that computes the branch target
MemRead | None | Data memory contents designated by the address input are put on the Read data output
MemWrite | None | Data memory contents designated by the address input are replaced by the value on the Write data input
MemtoReg | The value fed to the register Write data input comes from the ALU | The value fed to the register Write data input comes from the data memory
lw
R-type
lw, R-type
sw, beq
R-type, beq
lw, sw
beq taken
R-type, lw, sw, beq untaken
lw
R-type, sw, beq
R-type, lw, beq
sw
R-type
lw
Fig. 4.18 The setting of the control lines is completely determined by the opcode fields of the instruction.

## Slide 23
Designing the main control unit (Cont.)
  The datapath with multiplexors and control signals (Cont.)
    All 9 control signals can now be set on the basis of opcode to the control unit
Fig. 4.17 The simple datapath with the control unit.
PCSrc

## Slide 24
Designing the main control unit (Cont.)
  Operation of the datapath
    R-type instruction: add $t1, $t2, $t3
      The instruction is fetched, PC is incremented
      $t2 and $t3 are read from the register file; main control unit sets control lines
      The ALU operates, using the funct field of the instruction (bits 5:0) to generate the ALU function
      The result from the ALU is written into the register file (bits 15:11)
    lw $t1, offset($t2)
      The instruction is fetched, PC is incremented
      $t2 is read from the register file; main control unit sets control lines
      The ALU performs addition to compute the address ($t2 + sign-extended offset)
      To read the data memory
      The data from the memory unit is written into the register file (bits 20:16)
    beq $t1, $t2, offset
      The instruction is fetched, PC is incremented
      $t2 and $t3 are read from the register file; main control unit sets control lines
      The ALU performs subtraction for equality comparison; the adder computes the branch target address (PC + sign-extended offset shifted left by 2)
      The Zero result from the ALU is used to decide which adder result to store into the PC

## Slide 25
Fig. 4.19 The datapath in operation for an R-type instruction such as add $t1, $t2, $t3.

## Slide 26
Fig. 4.20 The datapath in operation for a lw instruction.

## Slide 27
Fig. 4.21 The datapath in operation for a beq instruction.

## Slide 28
Designing the main control unit (Cont.)
  Finalizing control
    Truth table of the main control unit
      Input: the 6-bit opcode field Op [5:0]
      Output: 9 control lines
Fig. 4.22 The control function for the simple single-cycle implementation is completely specified by this truth table.

## Slide 29
Designing the main control unit (Cont.)
  Finalizing control (Cont.)
    Example: implementing jumps
      Jump address
        [31:28] of the current PC + 4, 26-bit immediate filed of the jump instruction, bits 002
      An additional control signal Jump
Fig. 4.24 The simple control and datapath are extended to handle the jump instruction.

## Slide 30
Why a single-cycle implementation is not used today
  The single-cycle design is inefficient
    CPI = 1
    The clock cycle is determined by the longest possible path in the machine
  Example: performance of single-cycle machines
    Problem
      Operation times
        Memory units 200 ps, ALU & adder 100 ps, register file read/write 50 ps
      Instruction mix
        25% loads, 10% stores, 45% ALU instruction, 15% branches, 5% jumps
      Implementation 1
        Every instruction operates in 1 clock cycle of a fixed length
      Implementation 2
        Every instruction executes in 1 clock cycle using a variable-length clock
      To compare the performance between implementations 1 and 2
Instruction class | Functional units used by the instruction class |  |  |  |  | Total
R-type | Instruction fetch | Register access | ALU | Register access |  | 400 ps
Load word | Instruction fetch | Register access | ALU | Memory access | Register access | 600 ps
Store word | Instruction fetch | Register access | ALU | Memory access |  | 550 ps
Branch | Instruction fetch | Register access | ALU |  |  | 350 ps
Jump | Instruction fetch |  |  |  |  | 200 ps

## Slide 31
Why a single-cycle implementation is not used today (Cont.)
  Example: performance of single-cycle machines (Cont.)
    Solution
      To compute the critical path for different instruction classes
      Clock cycle of implementation 1: 600 ps
      Clock cycle of implementation 2:
        600  25% + 550  10% + 400  45% + 350  15% + 200  5% = 447.5 ps
      Performance ratio:
  Using the single-cycle design with a fixed clock cycle
    Acceptable for small and simple instruction set
    The clock cycle is equal to the worst-case delay for all instructions
    Each functional unit can be used only once per clock
   Multicycle implementation
    Shorter clock cycle
    Each instruction requires multiple clock cycles to complete

## Slide 32: An Overview of Pipelining
Pipeline
  An implementation technique in which multiple instructions are overlapped in execution
Fig. 4.25 The laundry analogy for pipelining.

## Slide 33
Pipeline (Cont.)
  Observations of the laundry example
    Pipelining improves throughput without improving the time to complete a single task
    If all stages take about the same amount of time and there is enough work to do
     The speedup is equal to the number of stages in the pipeline
    The pipeline is not completely full at the beginning and end of the workload
     This start-up and wind-down affects performance when the number of tasks is not large compared to the number of stages in the pipeline
  Example: single-cycle vs. pipelined performance
    Problem
      8 instructions: lw, sw, add, sub, and, or, slt, beq
      Memory access: 200 ps ALU operation: 200 ps Register file R/W: 100 ps
      To compare the average time between instructions of a single-cycle implementation to a pipelined implementation
    Solution
      The pipeline execution clock cycle must have the worst-case clock cycle of 200 ps
      To execute three lw instructions
        The time between the 1st and 4th instruction: 2400 ps vs. 600 ps
        The total execution time: 2400 ps vs. 1400 ps

## Slide 34
Fig. 4.26 Total time for each instruction calculated from the time for each component.
Fig. 4.27 Single-cycle, nonpipelined execution in top vs. pipelined execution in bottom.
2400 ps
1400 ps

## Slide 35
Pipeline (Cont.)
  Pipelining speed-up discussion
    Assuming ideal conditions: the stages are perfectly balanced
    Under ideal conditions and with a large number of instructions
       The speedup is approximately equal to the number of pipe stages
      In previous example: 800 ps should be improved to 160 ps
    Pipelining involves some overhead
      The time per instruction in the pipelined processor will exceed the minimum possible
      The speed-up will be less than the number of pipeline stages
    In the previous example: 2400 ps  1400 ps
      3 lw instructions: speedup = 2400/1400  1.71
      1,000,003 lw instructions: speedup = 800,002,400/200,001,400  4
  Summary
    Pipelining improves performance by increasing instruction throughput, as opposed to decreasing the execution time of an individual instruction
    Instruction throughput is the important metric because real programs execute billions of instructions

## Slide 36
Designing instruction sets for pipelining
  MIPS instruction set is designed for pipelined execution
  Characteristics of MIPS instruction set
    All MIPS instructions are the same length
      Easier to fetch and decode instructions
      Intel x86 instruction set
        Instructions vary from 1~15 bytes
        To translate x86 instructions into simple micro-operation
        To pipeline the micro-operations rather than the native x86 instructions
    MIPS has only a few instruction formats, with the source register fields being located at the same place in each instruction
      The 2nd stage can begin reading the register file at the same time that the hardware is determining what type of instruction was fetched
    Memory operands only appear in loads and stores
      We can use the execute stage to calculate the memory address and then access memory in the following stage
    Operands must be aligned in memory
      A single data transfer instruction will not require two data memory accesses
      The requested data can be transferred in a single pipeline stage

## Slide 37
Pipeline hazards
  Hazards are situations in pipelining when the next instruction cannot execute in the following clock cycle
  Structural hazards
    The hardware cannot support the combination of instructions that we want to execute in the same clock cycle
    Example
      Suppose we had a single memory instead of two memories
      In the same clock cycle the 1st instruction is accessing data from memory while the 4th instruction is fetching an instruction from the same memory
lw $4, 400($0)
structural hazards

## Slide 38
Pipeline hazards (Cont.)
  Data hazards
    The pipeline must be stalled because one step must wait for another to complete
    Arising from the dependence of one instruction on an earlier one that is still in the pipeline
      add $s0, $t0, $t1
      sub $t2, $s0, $t3  3 clock cycles are wasted in the pipeline
    Compiler can remove data hazards but its results is not satisfactory
      These dependences happen too often
      The delay is too long to expect the compiler to rescue us from this dilemma
    Solution: forwarding/bypassing
      Adding extra hardware to retrieve the missing item early from the internal resource
      Forwarding paths are valid only if the destination stage is later in time than the source stage
Fig. 4.29 Graphical representation of forwarding.

## Slide 39
Pipeline hazards (Cont.)
  Data hazards (Cont.)
    Solution: forwarding/bypassing (Cont.)
      Forwarding cannot prevent all pipeline stalls
      Load-use data hazard
        The data being loaded by a lw instruction has not yet become available when it is needed by another instruction
      Pipeline stall (bubble)
        A stall initiated in order to resolve a hazard
Fig. 4.30 We need a stall even with forwarding when an R-format instruction following a load tries to use the data.

## Slide 40
Pipeline hazards (Cont.)
  Data hazards (Cont.)
    Example: reordering code to avoid pipeline stalls
      a = b + e; c = b + f;
      Original
        lw $t1, 0($t0) # load b
        lw $t2, 4($t0) # load e
        add $t3, $t1, $t2
        sw $t3, 12($t0)
        lw $t4, 8($t0) # load f
        add $t5, $t1, $t4
        sw $t5, 16($t0)
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  | 
lw |  | IF | ID | EX | MEM | WB |  |  |  |  |  |  | 
add |  |  |  | IF | ID | EX | MEM | WB |  |  |  |  | 
sw |  |  |  |  | IF | ID | EX | MEM | WB |  |  |  | 
lw |  |  |  |  |  | IF | ID | EX | MEM | WB |  |  | 
add |  |  |  |  |  |  |  | IF | ID | EX | MEM | WB | 
sw |  |  |  |  |  |  |  |  | IF | ID | EX | MEM | WB
b
e
f
bubble
bubble
bubble
bubble
bubble
bubble

## Slide 41
Pipeline hazards (Cont.)
  Data hazards (Cont.)
    Example: reordering code to avoid pipeline stalls (Cont.)
      Reordering
        lw $t1, 0($t0) # load b
        lw $t2, 4($t0) # load e
        lw $t4, 8($t0) # load f
        add $t3, $t1, $t2
        sw $t3, 12($t0)
        add $t5, $t1, $t4
        sw $t5, 16($t0)
    Each MIPS instruction writes at most one result and does this in the last stage of the pipeline
    Forwarding is harder if
      There are multiple results to forward per instruction
      There is a need to write a result early in instruction execution
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
lw | IF | ID | EX | MEM | WB |  |  |  |  |  | 
lw |  | IF | ID | EX | MEM | WB |  |  |  |  | 
lw |  |  | IF | ID | EX | MEM | WB |  |  |  | 
add |  |  |  | IF | ID | EX | MEM | WB |  |  | 
sw |  |  |  |  | IF | ID | EX | MEM | WB |  | 
add |  |  |  |  |  | IF | ID | EX | MEM | WB | 
sw |  |  |  |  |  |  | IF | ID | EX | MEM | WB
b
e
f

## Slide 42
Pipeline hazards (Cont.)
  Control hazards (branch hazard)
    Arising from the need to make a decision based on the results of one instruction while others are executing  branch instruction
      The instruction that was fetched is not the one that is needed
      The flow of instruction addresses is not what the pipeline expected
    Solution 1: stall
      To stall immediately after fetching a branch, and waiting until the pipeline determines the outcome of the branch
      Conservative option, slow
      Example
        Suppose the branch can be resolve in the 2nd stage
        If the branch cannot be resolved in the 2nd stage, we will see an even larger slowdown
Fig. 4.31 Pipeline showing stalling on every conditional branch as solution to control hazards.

## Slide 43
Pipeline hazards (Cont.)
  Control hazards (branch hazard) (Cont.)
    Solution 2: prediction
      Simple approach: always predict that branches will be untaken
        Untaken: pipeline proceeds at full speed
        Taken: pipeline stall
      Sophisticated version: branch prediction
Fig. 4.32 Predicting that branches are not taken as a solution to control hazard.

## Slide 44
Pipeline hazards (Cont.)
  Control hazards (branch hazard) (Cont.)
    Branch prediction
      To assume a given outcome for the branch and proceed from that assumption rather than waiting to ascertain the actual outcome
      Some branches predicted as taken and some as untaken
      Dynamic hardware predictor
        Making their guess depending on the behavior of each branch
        May change predictions for a branch over the life of a program
      When the guess is wrong
        To ensure the instructions following the wrongly guessed branch have no effect
        To restart the pipeline from the proper branch address
Pipeline overview summary
  Pipelining is a technique
    To exploit parallelism among instructions in a sequential instruction stream
      To increase the number of simultaneously executing instructions
      To increase the rate at which instructions are started and completed
    To improve instruction throughput rather than individual instruction execution time or latency
  Invisible to programmer

## Slide 45: Pipelined Datapath and Control
Pipelined datapath
  5 stages: IF, ID, EX, MEM, WB
    Up to 5 instructions will be in execution during any single clock cycle
Fig. 4.33 The single-cycle datapath (similar to Fig. 4.17).

## Slide 46
Pipeline datapath (Cont.)
  Pipeline register
    To retain the value of an instruction for its other four stages
    All instructions advance during each clock cycle from one pipeline register to the next
    The registers are named for the two stages separated by that register
    PC can be thought of as a pipeline register
      PC is part of the visible architectural state
Fig. 4.35 The pipelined version of the datapath in Fig. 4.33.

## Slide 47
Pipeline datapath (Cont.)
  Ex: lw goes through the 5 stages of pipelined execution
    Highlight of registers or memory
      Right half: read Left half: write
    Instruction fetch (IF)
      To read the instruction using the address in the PC and place in the IF/ID
      To increment PC by 4, save to PC and IF/ID

## Slide 48
Pipeline datapath (Cont.)
  Ex: lw goes through the 5 stages of pipelined execution (Cont.)
    Instruction decode and register file read (ID)
      The 16-bit immediate field of the instruction supplied from IF/ID is sign-extended to 32 bit
      Register numbers supplied from IF/ID is used to read two registers
      All above three values and PC are placed in the ID/EX

## Slide 49
Pipeline datapath (Cont.)
  Ex: lw goes through the 5 stages of pipelined execution (Cont.)
    Execute or address calculation (EX)
      Using the ALU to calculate the load address
        To add the contents of register 1 and the sign-extended immediate from the ID/EX
      ALU result is placed in the EX/MEM

## Slide 50
Pipeline datapath (Cont.)
  Ex: lw goes through the 5 stages of pipelined execution (Cont.)
    Memory access (MEM)
      To read the data memory using the address from the EX/MEM
      To load the data into the MEM/WB

## Slide 51
Pipeline datapath (Cont.)
  Ex: lw goes through the 5 stages of pipelined execution (Cont.)
    Write back (WB)
      To read the data from the MEM/WB
      To write the data into the register file

## Slide 52
Pipeline datapath (Cont.)
  Ex: sw goes through the 5 stages of pipelined execution
    Fig. 4.39 and 4.40
  Two key points in the pipelined datapath
    To pass something from an early pipe stage to a later pipe stage, the information must be placed in a pipeline register
      Otherwise the information is lost when the next instruction enters that pipeline stage
      For the sw instruction, the data been stored was first placed in the ID/EX and then passed to the EX/MEM
    Each logical component of the datapath can be used only within a single pipeline stage
      Otherwise a structural hazard will occur
  A bug in this design: the write register number of lw is not supplied!
   To preserve the destination register number in lw instruction
    lw must pass the write register number from the ID/EX through EX/MEM to the MEM/WB

## Slide 53
Fig. 4.41 The corrected pipelined datapath to properly handle the load instruction.

## Slide 54
Graphically representing pipelines
  Multiple-clock-cycle pipeline diagram
    Simpler, do not contain all the details
    Occupying the proper clock cycles
      Time advances from left to right
      Instructions advance from the top to the bottom
Fig. 4.43 Multiple-clock-cycle pipeline diagram of five instructions.
Fig. 4.44 Traditional multi-clock-cycle pipeline diagram of five instructions in Fig. 43.

## Slide 55
Graphically representing pipelines (Cont.)
  Single-clock-cycle pipeline diagram
    To show the details of what is happening within the pipeline during each clock cycle
    Typically the drawings appear in groups to show pipeline operation over a sequence of clock cycles
Fig. 4.45 The single-clock cycle diagram corresponding to clock cycle 5 of the pipeline in Fig. 4.43 and Fig. 4.44.

## Slide 56
Pipelined control
  To label the control lines
    Similar as those used in the single-cycle implementation
    No separate write signals for PC and pipeline registers
      PC and pipeline registers are written on each clock cycle
Fig. 4.46 The pipelined datapath of Fig. 4.41 with the control signals identified.

## Slide 57
Fig. 4.47 A copy of Fig. 4.12.
Fig. 4.48 A copy of Fig. 4.16.
Signal name | Effect when deasserted (0) | Effect when asserted (1)
RegDst | The register destination number for the Write register comes from the rt field (bits 20:16) | The register destination number for the Write register comes from the rd field (bits 15:11)
RegWrite | None | The register on the Write register input is written with the value on the Write data input
ALUSrc | The second ALU operand comes from the second register file output (Read data 2) | The second ALU operand is the sign-extended, lower 16 bits of the instruction
PCSrc | The PC is replaced by the output of the adder that computes the value of PC + 4 | The PC is replaced by the output of the adder that computes the branch target
MemRead | None | Data memory contents designated by the address input are put on the Read data output
MemWrite | None | Data memory contents designated by the address input are replaced by the value on the Write data input
MemtoReg | The value fed to the register Write data input comes from the ALU | The value fed to the register Write data input comes from the data memory
lw
R-type
lw, R-type
sw, beq
R-type, beq
lw, sw
beq taken
R-type, lw, sw, beq untaken
lw
R-type, sw, beq
R-type, lw, beq
sw
R-type
lw

## Slide 58
Pipelined control (Cont.)
  Control lines corresponding to 5 pipeline stages
    Instruction fetch & Instruction decode/register file read
      No optional control lines to set
    Execution/address calculation
      RegDst, ALUOp, ALUSrc
    Memory access
      Branch, PCSrc, MemRead, MemWrite
    Write back
      MemtoReg, RegWrite
Fig. 4.49 The values of the control lines are the same as in Fig. 4.18, but they have been shuffled into three groups corresponding to the last three pipeline stages.

## Slide 59
Pipelined control (Cont.)
  To implement control
    To extend the pipeline registers to include control information
    To create the control information during instruction decode
Fig. 4.50 The control lines for the final three stages.

## Slide 60
Fig. 4.51 The pipelined datapath of Fig. 4.46, with the control signals connected to the control portions of the pipeline registers.

## Slide 61: Data Hazards: Forwarding versus Stalling
Data hazards and forwarding
  Example
    sub $2, $1, $3
    and $12, $2, $5
    or $13, $6, $2
    add $14, $2, $2
    sw $15, 100($2)
    Value of $2 changes from 10 to -20 at CC5
      sw gets the correct value
      Maybe add can also get the correct value
      and, or get the incorrect value because dependence lines go backward in time
Fig. 4.52 Pipelined dependences in a five-instruction sequence using simplified datapaths to show the dependences.

## Slide 62
Data hazards and forwarding (Cont.)
  To resolve data hazards
    The design of the register file hardware
      Write: 1st half of the cycle Read: 2nd half of the cycle
      The read delivers what is written
    Forwarding
      To forward the data as soon as it is available to any units that need it before it is available to read from the register file
      The data is available at the end of the EX (R-type) or MEM (load) stage
      To forward the data to an operation in the EX stage
        ALU operation, effective address calculation
  To detect data hazards
    Hazard conditions
      1a: EX/MEM.RegisterRd = ID/EX.RegisterRs
      1b: EX/MEM.RegisterRd = ID/EX.RegisterRt
      2a: MEM/WB.RegisterRd = ID/EX.RegisterRs
      2b: MEM/WB.RegisterRd = ID/EX.RegisterRt
IF ID EX MEM WB
IF ID EX MEM WB
IF ID EX MEM WB
EX hazard
MEM hazard

## Slide 63
Data hazards and forwarding (Cont.)
  To detect data hazards (Cont.)
    Above example
      Dependence #1
        Hazard type 1a: EX/MEM.RegisterRd = ID/EX.RegisterRs = $2
      Dependence #2
        Hazard type 2b: MEM/WB.RegisterRd = ID/EX.RegisterRt = $2
      Dependence #3
        Not a hazard, the register file supplies the proper data
      Dependence #4: no data hazard
#2
#1
#3
#4

## Slide 64
Data hazards and forwarding (Cont.)
  To detect data hazards (Cont.)
    Above hazard condition is inaccurate
      If an instruction does not write registers, its forwarding is unnecessary
        Examining the WB control field of the pipeline register during the EX and MEM stages to determine whether RegWrite is asserted
      If $0 is used as destination register, its value will not be forwarded
        MIPS requires that every use of $0 as an operand must yield an operand value of 0
        Adding EX/MEM.RegisterRd  0 or MEM/WB.RegisterRd  0
  To forward the proper data
    The pipeline registers holding the
    data to be forwarded
      Adding multiplexors and controls
      to the input of the ALU
      Forwarding control is in the EX
      stage
Fig. 4.53 The dependences between the pipeline registers move forward in time, so it is possible to supply the inputs to the ALU needed by the and and or instructions by forwarding the results found in the pipeline registers.

## Slide 65
Fig. 4.54 The ALU and pipeline registers before and after adding forwarding.
Fig. 4.55 The control values for the forwarding multiplexors in Fig. 4.54.

## Slide 66
Data hazards and forwarding (Cont.)
  To forward the proper data (Cont.)
    Hazard detection and control signals
      EX hazard
        if (EX/MEM.RegWrite
        and (EX/MEM.RegisterRd  0)
        and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
        if (EX/MEM.RegWrite
        and (EX/MEM.RegisterRd  0)
        and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10
add $2, $1, $3 IF ID EX MEM WB
add $5, $2, $4 IF ID EX MEM WB
ID/EX.RegisterRs | EX/MEM.Register.Rd
$2 | $2
ID/EX.RegisterRs = EX/MEM.RegisterRd

## Slide 67
Data hazards and forwarding (Cont.)
  To forward the proper data (Cont.)
    Hazard detection and control signals (Cont.)
      MEM hazard (original)
        if (MEM/WB.RegWrite
        and (MEM/WB.RegisterRd  0)
        and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
        if (MEM/WB.RegWrite
        and (MEM/WB.RegisterRd  0)
        and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
lw $2, 0($1) IF ID EX MEM WB
add $3, $4, $5 IF ID EX MEM WB
add $6, $2, $7 IF ID EX MEM WB
ID/EX.RegisterRs | EX/MEM | MEM/WB.RegisterRd
$2 |  | $2
ID/EX.RegisterRs = MEM/WB.RegisterRd

## Slide 68
Data hazards and forwarding (Cont.)
  To forward the proper data (Cont.)
    Hazard detection and control signals (Cont.)
      MEM hazard (revised)
        EX and MEM hazards occurs simultaneously
         Want to use the most recent value
         Only forwards if EX hazard condition is not true
add $1, $1, $2 IF ID EX MEM WB
add $1, $1, $3 IF ID EX MEM WB
add $1, $1, $4 IF ID EX MEM WB
ID/EX.RegisterRs = EX/MEM.RegisterRd
ID/EX.RegisterRs | EX/MEM.Register.Rd | MEM/WB.RegisterRd
$1 | $1 | $1
ID/EX.RegisterRs = MEM/WB.RegisterRd

## Slide 69
Data hazards and forwarding (Cont.)
  To forward the proper data (Cont.)
    Hazard detection and control signals (Cont.)
      MEM hazard (revised)(Cont.)
        if (MEM/WB.RegWrite
        and (MEM/WB.RegisterRd  0)
        and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd  0)
        and (EX/MEM.RegisterRd = ID/EX.RegisterRs))
        and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
        if (MEM/WB.RegWrite
        and (MEM/WB.RegisterRd  0)
        and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd  0)
        and (EX/MEM.RegisterRd = ID/EX.RegisterRt))
        and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
        if (MEM/WB.RegWrite
        and (MEM/WB.RegisterRd  0)
        and (EX/MEM.RegisterRd  ID/EX.RegisterRs)
        and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
        if (MEM/WB.RegWrite
        and (MEM/WB.RegisterRd  0)
        and (EX/MEM.RegisterRd  ID/EX.RegisterRt)
        and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 70
Fig. 4.56 The datapath modified to resolve hazards via forwarding.

## Slide 71
Fig. 4.57 A close-up of the datapath in Fig. 4.54 shows a 2:1 multiplexor, which has been added to select the signed immediate as an ALU input.

## Slide 72
Data hazards and stalls
  Forwarding cannot resolve all data hazards
    An instruction tries to read a register following a lw that writes the same register
     Something must stall the pipeline for the combination of lw followed by an instruction that reads its result
Fig. 4.58 A pipelined sequence of instructions.

## Slide 73
Data hazards and stalls (Cont.)
  Hazard detection unit
    It operates during the ID stage to insert the stall between the load and its use
    Condition
      if (ID/EX.MemRead
      and ((ID/EX.RegisterRt = IF/ID.RegisterRs)
      or (ID/EX.RegisterRt = IF/ID.RegisterRt))) stall the pipeline
    The instruction in the IF stage must also be stalled
      To prevent the PC and IF/ID pipeline register from changing
      The instruction in the IF stage will continue to be read using the same PC
      The registers in the ID stage will continue to be read using the same instruction fields in the IF/ID pipeline register
    Instructions in EX, MEM, WB stages: nops
      An instruction that does no operation to change stage
  How to insert nops
    To deassert all 9 control signals in the EX, MEM, and WB stages
      To change the EX, MEM, and WB control fields of the ID/EX pipeline register to 0
      The changed control signals will percolate through the pipeline
      No registers or memories are written if the control values are all 0

## Slide 74
Data hazards and stalls (Cont.)
  How to insert nops (Cont.)
    Example
      and becomes a nop, and all instructions following and are delayed one cycle
      and and or repeat in clock cycle 4 what they did in clock cycle 3
      A stall bubble delays everything behind it
Fig. 4.59 The way stalls are really inserted into the pipeline.

## Slide 75
Fig. 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit.

## Slide 76: Control Hazards
Control hazard (branch hazard)
  The delay in determining the proper instruction to fetch
    An instruction must be fetched at every clock cycle to sustain the pipeline
    The decision about whether to branch doesn’t occur until the MEM stage
  Relatively simple and occur less frequently
Fig. 4.61 The impact of the pipeline on the branch instruction.

## Slide 77
Assume branch not taken
  Stalling until the branch is complete is too slow
  To predict the branch will be untaken
    To continue execution down the sequential instruction stream
    If the branch is taken
      To discard instructions that are being fetched and decoded
      Execution continues at the branch target
  To discard instructions (flush instructions)
    To deassert all 9 control signals
    To change three instructions in the IF, ID, and EX stages when the branch reaches the MEM stage
Reducing the delay of branches
  To reduce the cost of the taken branch
    If the branch execution is moved earlier in the pipeline, then fewer instructions need be flushed
    Many branches rely only on simple tests
      Do not require a full ALU operation but can be done with at most a few gates
    A separate instruction that uses an ALU to perform a comparison for a more complex branch decision

## Slide 78
Reducing the delay of branches (Cont.)
  To move the branch decision up
    Branch address calculation
      To move the branch adder from the EX stage to the ID stage
      To be performed for all instructions but only used when needed
    Branch decision evaluation
      To perform equality comparison in ID stage using XOR an OR gates
      Additional forwarding and hazard detection hardware
        To forward results to the equality test logic that operates during ID
      A data hazard can occur and a stall will be needed
        ALU instruction immediately preceding a branch
  To reduce the penalty of a branch to one instruction if the branch is taken
    To flush instructions in the IF stage
      IF.Flush is added to zero the instruction field of the IF/ID pipeline register
    The fetched instruction is transformed into a nop
IF ID EX MEM WB
pipeline stall (nop)
IF ID EX MEM WB
add $1, $2, $3
beq $1, $4, 100

## Slide 79
Reducing the delay of branches (Cont.)
  Example: pipelined branch
    Assumption
      The pipeline is optimized for branches that are untaken
      Branch execution is moved to the ID stage
    36 sub $10, $4, $8
    40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7  4 = 72
    44 and $12, $2, $5
    48 or $13, $2, $6
    52 add $14, $4, $2
    56 slt $15, $6, $7
    ...
    72 lw $4, 50($7)
    Only one pipeline bubble on a taken branch

## Slide 80
Fig. 4.62 The ID stage of clock cycle 3 determines that a branch must be taken, so it selects 72 as the next PC address and zeros the instruction fetched for the next clock cycle.

## Slide 81
Fig. 4.62 The ID stage of clock cycle 3 determines that a branch must be taken, so it selects 72 as the next PC address and zeros the instruction fetched for the next clock cycle.

## Slide 82
Dynamic branch prediction
  In an aggressive pipeline, a simple static prediction scheme may waste too much performance
  Prediction of branches at runtime using runtime information
    Prediction is a hint that we hope is correct
    Fetching begins in the predicted direction (taken or untaken)
  Branch prediction buffer (branch history table)
    A small memory indexed by the low-order address bits of branch
    To contain one or more bits indicating whether the branch was recently taken or not
    Several branches with the same low-order address bits will share the same entry in the branch prediction buffer
  Dynamic branch prediction schemes
    1-bit prediction scheme
      Using 1 bit to record and predict
      Example: loops and prediction
        Loop branch, branch taken 9 times and then untaken once
        Mispredict on the first and last loop iterations
        Prediction accuracy: 80%

## Slide 83
Dynamic branch prediction (Cont.)
  Dynamic branch prediction schemes (Cont.)
    2-bit prediction scheme
      Using 2 bits to record and predict
      A prediction must be wrong twice before it is changed
  A branch prediction buffer can be accessed during the IF stage
    Predict taken: the target address can be known as early as the ID stage
    Predict untaken: sequential fetching
    If the prediction turns out to be wrong, the prediction bits are changed based on the prediction scheme it used
Fig. 4.63 The states in a 2-bit prediction scheme.

## Slide 84
Dynamic branch prediction (Cont.)
  Branch delay slot
    The slot directly after a delayed branch instruction
    Compilers and assemblers try to place an instruction that always executes after the branch
      To make the successor instructions valid and useful
      Three ways to schedule the branch delay slot
Fig. 4.64 Scheduling the branch delay slot.

## Slide 85
Dynamic branch prediction (Cont.)
  Branch target buffer
    A structure that caches the destination PC or destination instruction for a branch
    Usually organized as a cache with tags
    More costly than a simple prediction buffer
  Correlating predictor
    Using information about both a local branch and the global behavior of recently executed branches
    Greater prediction accuracy for the same number of prediction bits
  Tournament branch predictor
    Multiple predictors for each branch
    A selection mechanism that chooses which predictor to enable for a given branch

## Slide 86
Example: comparing performance of several control schemes
  Problem
    To compare performance for single-cycle, multicycle, and pipelined
    Instruction mix
      25% loads, 10% stores, 11% branches, 2% jumps, 52% ALU instructions
    Functional unit times
      Memory access: 200 ps ALU operation: 100 ps Register file R/W: 50 ps
    Pipelined
      Half of the loads are immediately followed by an instruction that uses the results
      Branch delay on misprediction is 1 clock cycle
      ¼ branches are mispredicted
      Jumps always pay 1 full clock cycle (average time is 2 clock cycles)
  Solution
    Single-cycle
      Clock cycle: 200 + 50 + 100 + 200 + 50 = 600 ps CPI: 1
    Multicycle
      Clock cycle: 200 ps
      CPI: 0.25  5 + 0.1  4 + 0.11  3 + 0.02  3 + 0.52  4 = 4.12

## Slide 87
Example: comparing performance of several control schemes (Cont.)
  Solution (Cont.)
    Pipelined
      Clock cycle: 200 ps
      CPI
        Loads: 0.5  1 + 0.5  2 = 1.5
        Stores & ALU instructions: 1
        Branches: 0.75  1 + 0.25  2 = 1.25
        Jumps: 2
         0.25  1.5 + 0.1  1 + 0.11  1.25 + 0.02  2 + 0.52  1 = 1.17
    Average instruction time
      Single-cycle: 600  1 = 600 ps
      Multicycle: 200  4.12 = 824 ps
      Pipelined: 200  1.17 = 234 ps

## Slide 88
Fig. 4.65 The final datapath and control for this chapter.

## Slide 89: Exceptions
Preliminary
  Control is the most challenging aspect of processor design
    The hardest part to get right and make fast
  Exception vs. interrupt
    Events other than branches or jumps that change the normal flow of instruction execution
    Exception
      Any unexpected change in control flow without distinguishing whether the cause is internal or external
    Interrupt
      An exception that comes from outside of the processor
  To detect exceptional conditions and taking the appropriate action is often on the critical timing path of a processor

## Slide 90
How exceptions are handled in the MIPS architecture
  Execution of an undefined instruction, an arithmetic overflow
  When an exception occurs
    To save the address of the offending instruction in the exception program counter (EPC)
      To determine where to restart the execution of the program
    To transfer control to the operating system at some specified address
      To provide some service to the user program
      To take some predefined action in response to an overflow
      To stop the execution and report an error
      To terminate or continue the program
  To communicate the reason for an exception
    Using a Cause register to indicate the reason for the exception
    Vectored interrupts
      The address to which control is transferred is determined by the cause of the exception
      The addresses are separated by 32 bytes or eight instructions
      When the exception is not vectored
        A single entry point for all exceptions
        The OS decodes the status register to find the cause

## Slide 91
How exceptions are handled in the MIPS architecture (Cont.)
  To implement the exception system used in the MIPS architecture
    The single entry point being the address 80000180hex
    EPC register
      A 32-bit register used to hold the address of the affected instruction
    Cause register
      A 32-bit register used to record the cause of the exception
      Ex: 10: undefined instruction 12: arithmetic overflow
Exceptions in a pipelined implementation
  To treat exceptions as another form of control hazard
  Steps to deal with exception (using an arithmetic overflow as an example)
    To transfer control to the exception routine immediately
    To flush instructions that follow the instruction caused exception
      IF stage
        To zero the instruction field of the IF/ID pipeline register (turning into a nop instruction)
        Similar as steps for branch misprediction
      ID stage
        To zero control signals using the multiplexor already in the ID stage
        Similar as steps for stall
        ID.Flush is ORed with the stall signal from the hazard detection unit

## Slide 92
Exceptions in a pipelined implementation (Cont.)
  Steps to deal with exception (using an arithmetic overflow as an example) (Cont.)
    To flush instructions that follow the instruction caused exception (Cont.)
      EX stage
        EX.Flush is added to cause new multiplexors to zero the control lines
        To prevent the instruction in the EX stage from writing its result in the WB stage
    To start fetching instructions from location 80000180hex
      To add an additional input to the PC multiplexor that sends 80000180hex to the PC
    To stop or complete the instruction that caused the exception
      To stop execution in the middle of the instruction if necessary
      If the instruction requires to be eventually completed, the instruction will be restarted from the beginning after the exception is handled
    To save the address of the offending instruction in the EPC register
      In reality it saves the address +4
      The exception handling routine must first subtract 4 from the saved value

## Slide 93
Fig. 4.66 The datapath with controls to handle exception.

## Slide 94
Exceptions in a pipelined implementation (Cont.)
  Example: exception in a pipelined computer
    Instruction sequence
      40hex sub $11, $2, $4
      44hex and $12, $2, $5
      48hex or $13, $2, $6
      4Chex add $1, $2, $1
      50hex slt $15, $6, $7
      54hex lw $16, 50($7)
      …
    Instructions to be invoked on an exception
      80000180hex sw $25, 1000($0)
      80000184hex sw $26, 1004($0)
      …
    Assume an overflow exception occurs in the add instruction

## Slide 95
Fig. 4.67 The result of an exception due to arithmetic overflow in the add instruction.

## Slide 96
Fig. 4.67 The result of an exception due to arithmetic overflow in the add instruction.

## Slide 97
Exceptions in a pipelined implementation (Cont.)
  Multiple exceptions can occur simultaneously
    To prioritize the exceptions (by the hardware)
  I/O device requests and hardware malfunctions are not associated with a specific instruction
    The implementation has some flexibility as to when to interrupt the pipeline
  To match the exception to the instruction
    The EPC register captures the address of the interrupted instructions
    The Cause register records all possible exceptions in a clock cycle
    Knowing in which pipeline stage a type of exception can occur
      An undefined instruction is discovered in the ID stage
      Invoking the operating system occurs in the EX stage
    The difficulty of always associating the correct exception with the correct instruction in pipelined computers
      Imprecise interrupt (imprecise exception)
        An interrupt or exception that is not associated with the exact instruction that was the cause the interrupt or exception
        The operating system will determine which instruction caused the problem
      Precise interrupt (precise exception)
        An interrupt or exception that is always associated with the correct instruction

## Slide 98
The hardware and the operating system must work in conjunction to deal with exceptions
  Hardware
    To stop the offending instruction
    Let all prior instructions complete and flush all following instructions
    To set registers EPC and Cause
    To jump to a prearranged address
  Operating system
    To look at the cause of the exception and act appropriately
    For an undefined instruction, hardware failure, or arithmetic overflow
      To kill the program and return an indicator of the reason
    For an I/O device request or an OS service call
      To save the state of the program
      To perform the desired task
      To restore the program to continue execution
      To run another task in the case of I/O device requests
    The most frequent exceptions
      Page faults and TLB exceptions

## Slide 99: Parallelism via Instructions
Fig. 4.68 Static two-issue pipeline in operation.
Fig. 4.69 A static two-issue datapath.

## Slide 100
Fig. 4.70 The scheduled code as it would look on a two-issue MIPS pipeline.
Fig. 4.71 The unrolled and scheduled code of Fig. 4.70 as it would look on a static two-issue MIPS pipeline.

## Slide 101
Fig. 4.72 The three primary units of a dynamically scheduled pipeline.

## Slide 102
Fig. 4.73 Record of Intel Microprocessors in terms of pipeline complexity, number of cores, and power.

## Slide 103: Real Stuff: The ARM Cortex-A8 and Intel Core i7 Pipelines
Fig. 4.74 Specification of the ARM Cortex-A8 and the Intel Core i7 920.

## Slide 104
Fig. 4.75 The A8 pipeline.
Fig. 4.76 CPI on ARM Cortex A8 for the Minnespec benchmarks, which are small versions of the SPEC2000 benchmarks.

## Slide 105
Fig. 4.77 The Core i7 pipeline with memory components.

## Slide 106
Fig. 4.78 CPI of Intel Core i7 920 running SPEC2006 integer benchmarks.

## Slide 107
Fig. 4.79 Percentage of branch midpredictions and wasted work due to unfruitful speculation of Intel Core i7 920 running SPEC2006 integer benchmarks.

## Slide 108: Fallacies and Pitfalls
Fallacies
  Pipelining is easy
    Correct pipeline execution is very subtle
    The Verilog to describe a pipeline like that in the Intel Core i7 will be thousands of lines
  Pipelining ideas can be implemented independent of technology
    The delayed branch is now redundant with longer pipelines, superscalar execution, and dynamic branch prediction
    In the early 1990s
      Dynamic pipeline scheduling took too many resources and was not required for high performance
    As transistor budgets continued to double due to Moore’s Law
      Logic became much faster than memory
      Multiple function units and dynamic pipelining made more sense
    Today
      Concerns about power are leading to less aggressive designs

## Slide 109
Pitfalls
  Failure to consider instruction set design can adversely impact pipelining
    Many difficulties of pipelining arise because of instruction set complications
    Widely variable instruction lengths and running times
      Can lead to imbalance among pipeline stages and severely complicated hazard detection
      Solution: micro-operations and micro-pipelined scheme
    Sophisticated addressing modes
      Addressing modes that update registers complicate hazard detection
      Addressing modes that require multiple memory accesses substantially complicate pipeline control